## Slide 1
Modeling and Measuring Ultrasonic Nondestructive Evaluation Systems
This is a course organized by Lester W. Schmerr Jr., Professor Emeritus in Aerospace Engineering at Iowa State University. The content is based primarily on the book, Ultrasonic Nondestructive Evaluation Systems – Models and Measurements, authored by Prof. Schmerr and Prof. Sung-Jin Song, so that the reader is encouraged to purchase this book to enhance the value of the course.
The course contains annotated Power Point Slides that have been combined into this single pdf document that can be read on this website. The individual PowerPoints are also available for download.
Homework problems are also part of the course. The problem numbers are listed near the end of the sections where the appropriate topics are discussed. All of the course homework problems and solutions are available in a homework manual, which can either be read on this website or downloaded.
Matlab is used extensively in the course and homework to illustrate concepts and generate results. The Matlab course, homework, and book m-files are also available on this website for download.
The purpose of this course is to introduce the physics and mathematics behind ultrasonic flaw inspections so that one can understand the nature of the signals that are produced and how they are related to the flaws present. Linear systems theory, theory of elastic waves, and Fourier analysis serve as the foundations for much of the course. The course also covers briefly some aspects of statistical pattern recognition and probabilistic decision-making, and neural networks.

## Slide 2
A Personal Preface (L.W. Schmerr)
As a graduate student in the Department of Mechanics at the Illinois Institute of Technology in the mid to late 60’s I was trained in the area of elastic waves. After graduation, I went to Iowa State University in 1969 as an Assistant Professor in Engineering Mechanics. There, I started looking for a research area on which I could build a career. In the early 70’s I participated in an NSF summer faculty program where I worked with the Nondestructive Testing group at General Dynamics, Fort Worth, Texas and where I was introduced to ultrasonics as a tool to inspect materials and to find flaws. At one point during the summer our group had a meeting with a General Dynamics corporate executive. After we had described our work, he asked us what we actually measured in an ultrasonic test. At that point in time I realized that there was simply not a good answer to his question and that finding one could be an important and interesting endeavor. Subsequently, modeling ultrasonic inspections became my main area of study which has endured to this day. In fact, this course is a snapshot of much of what I have learned over the years as to what we actually do measure in ultrasonic NDE.
As described in this course, we now do have reasonably good models of all the elements in an ultrasonic inspection. There were several key advances that serve as a foundation for these efforts. In 1979, Bert Auld from Stanford University developed a very general model of an inspection, based upon electrical and mechanical reciprocity principles, that could be used, in conjunction with elastic wave propagation and scattering models to predict ultrasonic signals received from flaws. However, while the Auld model is very general it does not relate those signals directly to any flaw properties being measured.

## Slide 3
In 1983, Bruce Thompson and Tim Gray at the Center for NDE, Iowa State University, used the Auld model to develop a reduced model for “small” flaws (where the incident waves could be assumed to be a constant over the flaw geometry). This Thompson-Gray model, while less general than the Auld model, had the major advantage of explicitly delineating the flaw scattering response as a part of the entire ultrasonic measurement. Thompson and Gray also showed how this flaw response part (called the far field scattering amplitude) could be obtained by measuring what they called the “system efficiency factor” (in this course a very closely related factor is called the “system function”) in a reference experiment, and then extracting the flaw response through deconvolution.
The Auld and Thompson-Gray models give us some general frameworks to model ultrasonic NDE inspections but there are many questions that remain. For example, how do the individual measurement system components (pulser/receiver, cabling, transducer(s) ) affect the measured response? What are effective models to predict the waves generated by ultrasonic transducers? How is the far field flaw scattering amplitude obtained from the Thompson-Gray measurement model related to the actual geometry and material characteristics of the flaw? You will learn some answers to these and other important questions in this course.
The three books on modeling ultrasonic NDE inspections that I have written over the last 20 or so years can give you many of the modeling tools needed to predict flaw responses. However, the ability to extract specific flaw information (size, shape, properties, etc.) from those responses remains an area ripe for further investigation. Thus, at the end of this course I have included some lessons on statistical pattern recognition and neural networks. These areas can provide powerful tools for answering many of the very difficult questions that remain as to what we actually measure and how we can use those measurements to make rational engineering decisions from our ultrasonic NDE inspections.

## Slide 4
I would like to close with a few words about my career. There are three accomplishments that I would like to highlight that I feel have contributed significantly to our understanding of ultrasonic tests. First, I reformulated Auld’s model based on purely mechanical reciprocity principles. This is important since the elastic wave propagation and scattering elements in Auld’s model are purely mechanical terms and by treating them as such one can see more clearly how they are imbedded in the entire measurement process through an acoustic/elastic transfer function. The details of this form of Auld’s model are given in this course. I also showed how an ultrasonic transducer can be characterized as an electrical impedance and a sensitivity and how these factors can be obtained from a set of purely electrical measurements of the transducer in a pulse-echo setup. This greatly simplifies the previous procedures used in the acoustics literature which relied on a complex set of measurements involving multiple transducers. These details are also included in this course. In ultrasonic phased array inspections, one often uses those arrays to generate flaw images. A third accomplishment is not described in this course but is described in my book, Fundamentals of Ultrasonic Phased Arrays. There, I showed how three commonly used flaw imaging methods -the synthetic aperture focusing technique (SAFT), the total focusing method (TFM), and the Physical Optics Far-Field Scattering (POFFIS) method – are ad-hoc models that can be made more rational by inverting the Thompson-Gray measurement model to obtain a “Imaging Measurement Model”. This model explicitly describes what these images generated by ultrasonic phased arrays represent in terms of the reflectivity and geometry of the flaws being imaged.
Although I have worked in ultrasonic NDE for many years, one of my most cited papers comes from my work on use of hypersingular integrals in the boundary element method (Krishnasamy, G., Schmerr, L.W., Rudolphi, T.J. and Rizzo, F.J., "Hypersingular boundary integral equations: some applications in acoustics and elastic wave scattering," Trans. ASME, Journ. of Appl. Mechanics, 57, 404-414, (1990).)

## Slide 5
Although this paper is not on ultrasonic NDE per se, it is related since the integral equations governing the scattering of cracks are hypersingular. I will end by noting that is also somewhat ironic that the only paper that I have written that has received an award is not on ultrasonic NDE but on the use of neural networks in conjunction with eddy current inspections (American Society of Nondestructive Testing 1992 Achievement Award "in recognition of a manuscript that represents an outstanding contribution to the advancement of NDT" : Mann, J.M., Schmerr, L.W., and J.C. Moulder, "Inversion of eddy current data using neural networks," Materials Evaluation, 49, 34-39, 1991.)
The content of the course is mostly from my second book on ultrasonics but there are many results stated without proof in this course whose details can be found in my other two books. The references for all three books are:
Schmerr, L.W. and S.J. Song, Ultrasonic Nondestructive Evaluation Systems – Models and Measurements, Springer, 2007.
Schmerr, L.W., Fundamentals of Ultrasonic Nondestructive Evaluation – A Modeling Approach, 2nd Ed.
Springer, 2016.
Schmerr, L. W., Fundamentals of Ultrasonic Phased Arrays, Springer, 2015.

## Slide 6
TABLE OF CONTENTS
1 Introduction to Ultrasonic Nondestructive Evaluation Systems Page 9
2 Introduction to Matlab 25
3 Ultrasonic System Overview (Chapter 1) 52
4 The Fourier Transform (Appendix A) 69
5 The Fast Fourier Transform (FFT) and Matlab Examples (Appendix A) 88
6 Impedance Concepts and Thévenin Equivalent Systems (Appendix B) 129
7 Pulser Characteristics – Models and Measurements (Chapter 2) 153
8 Linear Electrical and Acoustic Systems – Some Basic Concepts (Appendix C) 176
The topics of the course are listed below as well as the Chapters or Appendices of the book,
Ultrasonic Nondestructive Evaluation Systems – Models and Measurements that correspond to
the topics covered.

## Slide 7
9 Cabling – Models and Measurements (Chapter 3) 199
10 Transducer Modeling (Chapter 4) 211
11 Wave Propagation Fundamentals -1 (Appendix D)
Propagation of Plane and Spherical Waves 235
12 Wave Propagation Fundamentals -2 (Appendix D)
Reflection and Transmission 254
13 Wave Propagation Fundamentals -3 (Appendix D)
Ultrasonic Attenuation 277
14 Waves Used in NDE (Appendix E) 293
15 Acoustic/Elastic Transfer Function (Chapter 5) 316
16 The Ultrasound Reception Process (Chapter 5) 330
17 Transducer Characterization (Chapter 6) 351

## Slide 8
18 The System Function (Chapter 7) 371
19 Transducer Sound Radiation (Chapter 8) 386
20 The Paraxial Approximation (Chapter 8) 429
21 Gaussian Beams and Transducer Modeling (Appendix F, Chapter 9) 440
22 Flaw Scattering Models (Chapter 10) 486
23 Ultrasonic System Measurement Model – I (Chapter 11) 556
24 Ultrasonic System Measurement Model – II (Chapter 11) 577
25 Measurement Model Examples (Chapter 11) 611
26 Special Topics –I
Dispersion 616
27 Statistical Foundations of Pattern Recognition 624
28 Neural Networks 676