## Slide 1
Impedance Concepts and
Thévenin Equivalent Systems
Notes: We will see several examples where the concept of impedance is important and examine the concept of Thevenin equivalent systems.

## Slide 2
Learning Objectives
Electrical impedance
Description of 1-D waves in a fluid
equation of motion/constitutive equation
plane waves - pulses and harmonic waves
frequency and wavelength
acoustic impedance
Thévenin equivalent electrical circuits
Notes: Electrical impedance is a property you may already be familiar with. We will see that impedance is also defined for the waves present in ultrasonic system and examine some basic characteristics of waves. Finally, we will discuss the concept of Thevenin equivalent electrical circuits.

## Slide 3
resistor
capacitor
inductor
V(t)
I(t)
Concept of Impedance
basic circuit elements
Notes: Some of the basic elements often seen in circuits include resistors, capacitors, and inductors. In each of these elements we can define the relationship between the voltage acting across the element in terms of the current flowing through the element.

## Slide 4
resistor
capacitor
inductor
general
impedance
For alternating (harmonic) voltages and currents
electrical impedance Z = Ze (ohms)
Notes: For alternating voltages and currents we can relate the voltages and current in these elements through a complex electrical impedance, Z, which in general can also be a function of the frequency. We will place an e superscript on Z to indicate it an electrical impedance and to distinguish it from other impedances we will discuss shortly.

## Slide 5
1-D plane wave traveling wave in a fluid
p
dx
dz
dy
Equation of motion
p(x, t ) … pressure in the fluid
r … fluid density
vx (x, t) … velocity
Notes: We will see that impedance is also defined for other types of non-electrical problems. Since ultrasonic NDE involves waves propagating in fluids and solids, let us consider some aspects of wave propagation before we define the concept of wave impedance. First, let us consider the problem of waves propagating in a fluid where all the motion of the wave is in the x-direction and the pressure in the wave only depends on x . Since the pressure is a constant in the y-z plane this is a 1-D plane wave. If we examine Newtons law F = ma for a small element of the fluid we can derive the equation of motion which relates the derivative of the pressure to the acceleration of the fluid element.

## Slide 6
Constitutive equation
K … compressibility of the fluid
… displacement
1-D wave
equation
wave speed in the
fluid
dx
dux
= relative change in volume
(volumetric strain)
Notes: For an ideal fluid the pressure is linearly related to the displacement gradient of the element which is also equal to the so-called volumetric strain. The proportionality constant in this constitutive equation is called the compressibility, K, of the element. If we take the derivative of Newtons law with respect to x and use the constitutive equation we arrive at the 1-D wave equation for the pressure, where a new constant, called the wave speed , appears.

## Slide 7
1-D plane wave solutions
f
g
Harmonic waves
x
Notes: The 1-D wave equation has 1-D traveling plane wave solutions where we can have pressure waves defined by arbitrary functions that travel in the plus or minus x-direction. As a special case we can let those functions be harmonic traveling waves.

## Slide 8
1-D plane harmonic wave traveling in the +x-direction
Fourier transform pair
Let
then
Thus, v(t) is a superposition of plane waves
(1)
Notes: Now let us examine the Fourier transform and inverse Fourier transforms for a spectrum that has the particular harmonic wave form shown in Eq. (1). Then we see the inverse Fourier transform represents a superposition of 1-D traveling harmonic waves. What is the corresponding time domain signal that we recover from this inverse Fourier transform?

## Slide 9
where
Now, let
Then
so
Thus, we can always synthesize a traveling plane wave pulse with a superposition of harmonic plane waves.
Notes: By simply changing to a different variable we can see that if a time domain waveform v(t) has a frequency domain spectrum V(f) then if we superimpose traveling harmonic waves with amplitude V(f) we recover from the inverse FFT a traveling pulse with the same waveform as v. This is shown above for a wave traveling in the plus x-direction but a similar result holds for a wave traveling in the negative x-direction. Thus, we can always work with harmonic waves in describing NDE systems since we can recover the corresponding pulses present in those systems simply by performing an inverse FFT of the harmonic wave solutions.

## Slide 10
various forms of a harmonic plane wave
traveling in the +x-direction
f ... frequency (cycles/sec)
w …frequency (rad/sec)
k … wave number (rad/length)
l …wavelength (length/cycle)
Notes: A traveling harmonic plane wave can be written in a number of different forms, all of which are equivalent. The form indicated by the red arrow is one form uwe will use frequently in solving wave problems.

## Slide 11
magnitude of the pressure at a fixed x versus time, t:
T… period (sec/cycle)
frequency (cycles/sec)
rad/cycle
circular frequency (rad/sec)
t
(1)
Notes: The period T of a harmonic wave is the time it takes for the waveform to go through a complete cycle of 2π radians so by examining the phase term involving time in the wave ( see Eq. (1) ) as we hold x fixed we obtain the result that the frequency (in cycles/sec) is just the reciprocal of the period. The circular frequency is just 2π times the frequency in cycles/sec since there are 2π radians in a cycle.

## Slide 12
magnitude of the pressure at a fixed time, t, versus distance, x:
x
l ... wavelength (length/cycle)
spatial frequency (cycles/length)
rad/cycle
spatial circular frequency
(wave number) (rad/length)
Notes: If instead we hold the time fixed and plot the pressure versus x we again seen a sinusoidal curve. The distance during one cycle is the wavelength which acts like the period does in time so the reciprocal of the wavelength acts like a spatial frequency. If we multiply that spatial frequency by 2π we get a spatial circular frequency called the wavenumber, k.

## Slide 13
magnitude of the pressure at a fixed time, t, versus distance, x:
x
l ... wavelength (length/cycle)
fundamental relationship that shows how the frequency of a plane harmonic traveling wave is related to its wavelength
(1)
Notes: If we hold the time fixed and vary the x-location over one complete cycle (2pi radians), by definition we go through a distance, λ , equal to the wavelength of the wave, so that from Eq. (1) we find that the frequency (in cycles/sec) time the wavelength is just the wave speed.

## Slide 14
Example:
consider a 5MHz plane wave traveling in water ( c =1500m/sec).
What is the wave length?
Notes: Here is an example of the wavelength for a 5 MHz wave traveling in water. Thus, we see the wavelengths in NDE tests are typically quite small.

## Slide 15
For a plane pressure wave traveling in the x-direction
Let
then
Notes: If we consider a plane wave traveling in the x-direction, we can place that plane wave into Newton’s law and integrate to find the x-velocity, which we see is just proportional to the pressure

## Slide 16
specific acoustic impedance
of a plane wave (pressure/velocity)
acoustic impedance
of a plane wave
(force/velocity)
x
S … area
For more general (harmonic) waves
Notes: The ratio of the pressure to the velocity is a quantity called the specific acoustic impedance of the plane wave. If we multiply that specific acoustic impedance by an area of the wavefront then the ratio of the force in the wave over that area to the velocity is called the acoustic impedance of the plane wave. This impedance, F/v, plays the same role for the wave as the voltage to current ratio, V/I, plays in an electrical circuit. To distinguish this impedance, Z, from an electrical impedance we will place an “a” superscript on it to indicate it is an acoustic impedance. Although the acoustic impedance of a plane wave is a constant, for other types of waves the acoustic impedance, like the electrical impedance, can be a function of the frequency.

## Slide 17
Vi
R1
C1
R2
L1
R3
V
Thévenin equivalent circuit (harmonic voltages and currents)
Vs(w)
Zeq(w)
V
I
I
Notes: The reason that the concept of impedance is so important is because if we take a linear electrical system of components, such as the one shown, we can replace it by an equivalent system consisting only of a voltage source and an impedance, called a Thevenin equivalent system. Both systems are equivalent because if both systems are terminated in some fashion (as shown by the dotted lines) the voltage and current outputs are identical. We will not prove this equivalence here.

## Slide 18
Determining the Thévenin equivalent source
Vs(w)
Zeq(w)
V0
open-circuit voltage
Determining the Thévenin equivalent impedance
Vs(w)
Zeq(w)
RL
VL
(1)
Notes: We can determine the Thevenin equivalent system in two steps. First, if we measure the open circuit output voltage of the system, this will just be the equivalent voltage source acting. Then if we place a known impedance (such as the resistance shown above) at the output and measure the output voltage across this known resistance, then we can find the equivalent impedance as shown in Eq. (1) above.

## Slide 19
Example: find the Thévenin equivalent circuit for
the following circuit
Vi
R
C
Notes: As an example of determining a Thevenin equivalent system, consider a simple circuit consisting of a known voltage source and a resistance and capacitance.

## Slide 20
Vi
R
C
I
open-circuit voltage
eliminating I, we find
Thévenin equivalent source
Notes: If we examine the voltages and current acting across the resistor and capacitor under open circuit conditions then we can eliminate the current and obtain an expression for the open circuit voltage, which is just the Thevenin equivalent voltage source.

## Slide 21
Vi
R
C
I1
RL
I2
VL
eliminating I1 , I2 gives
so
(1)
Notes: Similarly, if we place a known resistance at the output terminals and relate the voltages across the resistances and capacitance to the currents flowing, we can eliminate those currents and find the voltage ,VL, across the known resistance. Equation (1) then gives us the Thevenin equivalent impedance

## Slide 22
Vi(w)
R
C
Notes: Thus, the original electrical system is equivalent to the Thevenin equivalent system shown.

## Slide 23
In many EE books the equivalent impedance is obtained by simply shorting out (removing) the source and examining the ratio V/I at the output port:
R
C
I1
I
Notes: In an electrical engineering course on circuits you may see another approach to obtaining the Thevenin equivalent impedance where we imagine shorting out the known source and then simply examine the ratio of the output voltage and current. As shown above, this does give the correct impedance but it obviously is not practical (or wise) to physically short out the source in a real instrument. Experimentally, we must use the previous approach, which only requires the measurement of VL and the open circuit voltage.

## Slide 24
Homework problem
B.3
Notes: Homework problem from Appendix B.