## Slide 1
Transducer Modeling
Notes: Transducers are obviously a very important part of any ultrasonic system. Here we examine models of a transducer when it is used to generate ultrasound.

## Slide 2
Learning Objectives
Two port and three port transducer models
Sittig model
Mason model
KLM Model
Acoustic radiation impedance
Transducer sensitivity, impedance
The sound generation process
Notes: There are a variety of transducer models available that we will examine. We will see that three key parameters associated with the transducer are the acoustic radiation impedance, its electrical impedance and its sensitivity. In this section we will also combine our pulser, cabling and transducer models into a complete representation of the sound generation process in an ultrasonic setup.

## Slide 3
Transducer model - fields
Reciprocity :
Consider a P-wave
immersion
transducer:
pressure,
velocity fields
p, v
V
I
n
(1)
Notes: We can consider a sending immersion transducer as a “mixed” model where we take the electrical inputs as lumped parameters of voltage and current but take the outputs as the pressure and velocity fields on the face of the transducer in contact with the fluid. If we assume the transducer is a reciprocal device then we can relate these parameters through the reciprocity relation of Eq. (1)

## Slide 4
voltage
current
compressive force
velocity, v(x,w)
Transducer model- ‘lumped’ parameters
so reciprocity becomes:
For
piston
behavior
pressure, p(x,w)
Notes: If we assume the velocity of the transducer face is a constant, then this is a “piston” transducer model and we can replace the integrals of the pressure fields in the reciprocity relations by compressive force terms and write the reciprocity relationship entirely in terms of lumped quantities of (voltage, current) and (force, velocity)

## Slide 5
[TA]
V
I
F
v
Transducer model - transfer matrix
2-Port Transducer Model
From reciprocity
force
velocity
A
Notes: If the transducer is a linear, reciprocal device we can thus relate the lumped inputs and outputs through a two port 2x2 transfer matrix whose determinant must be equal to one.

## Slide 6
I
[TA]
V
F
v
Transducer model - transfer matrix
Sittig model:
Notes: There is an explicit model of the transducer 2x2 transfer matrix called the Sittig model, where the overall transfer matrix is written in terms of the product of two separate transfer matrices, as shown.

## Slide 7
Transducer model - transfer matrix
wave number of piezoelectric plate
wave speed of the plate, defined in terms of:
plate elastic constant at constant flux density
plate density
constant, defined in terms of:
plate stiffness
clamped capacitance, defined in terms of:
plate area, thickness
plate dielectric impermeability at constant
strain
plate acoustic impedance
backing acoustic impedance
Notes: There are many parameters in the Sittig model since the transducer is inherently a complex electromechanical device.

## Slide 8
Transducer - three port model
I
V
F2 , v2
F1 , v1
transducer crystal
Plating
(thickness neglected)
V
I
F2
v2
F1
v1
3x3 impedance matrix
Notes: The Sittig model assumes the piezoelectric crystal in the transducer has some material backing on its inside face. If we do not include such backing in a transducer model then we can consider the transducer as a three port system where we have the driving electrical port and acoustic ports on both the front and back faces of the crystal. For such a three port system we can model the system through a 3x3 impedance matrix. Such a system is very useful when we want to design a transducer with specific characteristics as we can also change the backing on the crystal as part of the design.

## Slide 9
Transducer - Mason equivalent circuit
v1
v2
V
I
F1
F2
1: n
C0
- C0
iZ0 /sin(kl)
a
- iZ0 tan(kl/2)
a
- iZ0 tan(kl/2)
a
Notes: One frequently used equivalent circuit model of such a three port system is the Mason model shown here. Some designers do not like this model because it includes a non-physical negative capacitance term.

## Slide 10
Transducer - KLM equivalent circuit model
1 : f
- i X
C0
V
I
F1
v1
F2
v2
l/2
l/2
Z0
Z0
a
a
f =
2M sin(kl/2)
1
X = Z0 M2 sin(kl)
a
M = h33 / (wZ0 )
a
Notes: Another equivalent three port circuit model of a transducer is the KLM model.

## Slide 11
Sittig model with crystal facing layers
Backing (Zb )
a
crystal
facing layers
(epoxy bonding, wear plate, etc.)
Acoustic layer:
F1
v1
F2
v2
[Tl]
Commercial transducer:
[TA] = [TA] [TA] [Tl] ...
e
a
Notes: The Sittig, Mason, and KLM model have all been successfully used for designing ultrasonic transducers. Because the Sittig model involves 2x2 transfer matrices, it is particularly easy to add elements such as wear plates since we have seen that such acoustic layers can be characterized as 2x2 acoustic transfer matrices that can simply be concatenated through multiplication with the other transfer matrices.

## Slide 12
[TA]
V
I
Ft
v
Transducer – radiation into a fluid
At the acoustic port the force and velocity parameters
are not independent. We can write
… acoustic radiation impedance (a "lumped"parameter
that depends on the velocity and pressure distribution
at the acoustic port, the port geometry, and the fluid properties)
A
Notes: When an immersion transducer is used in practice, its acoustic output port is always inherently terminated, i.e. the output compressive force and the velocity are related to one another through an acoustic radiation impedance. This acoustic impedance is a function of the acoustic waves radiated by the transducer so we will have to discuss some elements of those acoustic waves, which we will do here briefly. Later, we will examine those waves in more detail and justify some of the results that are simply given here.

## Slide 13
Acoustic radiation impedance
Rayleigh-Sommerfeld integral model of radiation of
waves into a fluid by a piston transducer
x
y
r… fluid density
c … fluid wave speed
k = w/c
pressure
Notes: As we will see later we can model the pressure waves generated in a fluid by a piston transducer in terms of a Rayleigh-Sommerfeld integral (also called a Rayleigh integral by some authors) over the face of the transducer. Since the compressive force generated is an integral of this pressure over the face of the transducer, we can write an explicit expression for the acoustic radiation impedance in terms of two surface integrals.

## Slide 14
Greenspan, 1979: showed that for a circular piston transducer of radius a the acoustic radiation impedance obtained from the Rayleigh-Sommerfeld model could be found explicitly in the form
.
J1 … Bessel function
S1 … Struve function
SA = pa2
Acoustic radiation impedance
Notes: However, we do not have to do those integrals directly since Greenspan has shown that for a circular piston transducer we can express those integrals in terms of a Bessel function and a Struve function, which are two well-known special functions whose numerical evaluation is straightforward.

## Slide 15
Acoustic radiation impedance
>> ka=linspace(0, 25, 100);
>> ka = ka + eps*( ka ==0);
>> Z = 1 -(besselj(1,2*ka)-i*struve(2*ka))./ka;
>> plot(ka, abs(Z))
Greenspan model of a circular piston transducer
0
5
10
15
20
25
0
0.2
0.4
0.6
0.8
1
1.2
1.4
Notes: Here is a plot of the normalized radiation impedance of a circular piston transducer of radius a, as a function of the nondimensional wavenumber (frequency). We see at larger ka values the acoustic radiation impedance becomes nearly a constant. Here SA is the area of the face of the transducer. Shown also is the MATLAB code used for evaluation of this plot. The Bessel function can be calculated with a built-in MATLAB function besselj. The struve function will be given on the next slide.

## Slide 16
function y = struve(z)
num = length(z);
y=zeros(1,num);
for k = 1:num
y(k) = quadl(@struve_arg, 0, 1, [ ],[ ], z(k));
end
function y = struve_arg(x, z)
y = (4./pi).*z.*x.^2.*sin(z.*(1-x.^2)).*sqrt(2-x.^2);
Acoustic radiation impedance
this uses
Notes: Here is the evaluation of the Struve function in MATLAB.

## Slide 17
velocity
Acoustic radiation impedance
Most NDE transducers operate at high frequencies (ka >> 1). At such high frequencies, if we can
assume piston behavior, for any shaped transducer it can be shown that
density, wave speed, area
A
pressure distribution
Notes: Most NDE transducers operate at high frequencies and we can show that in fact the acoustic radiation impedance for any such high frequency transducer (not just a circular one) is equal to the acoustic plane wave impedance, which is the product of the density of the fluid times its wave speed times the area of the face of the transducer. Since this acoustic radiation impedance is a known constant, when dealing with a sending transducer we can always treat it as a terminated system where we know the value of that acoustic termination.

## Slide 18
Sensitivity, Impedance
Vin
Iin
the electrical characteristics of the transducer
can be completely described by its input
impedance:
Iin
Vin
A
Notes: Unlike a cable, it is very difficult to measure the 2x2 transfer matrix that characterizes a transducer because one port is an acoustic port where it is not simple to measure either force or velocity. However, because the transducer is always terminated with a known acoustic impedance, as shown above, we will see that we do not have to measure all the transfer components directly. For example, we can easily measure the voltage and current at the input electrical port, whose ratio gives us the transducer electrical impedance. This electrical impedance tells us how the transducer electrically terminates the cable it is connected to.

## Slide 19
Sensitivity, Impedance
The particular sensitivity we will use is:
to describe the conversion of electrical signals into acoustic signals, we could use the transducer's sensitivity, SOI, where
O … an output (force or velocity)
I … an input (voltage or current)
A
Notes: If, in addition to knowing the electrical termination (impedance) characteristics of the transducer, we also have a measure of how the electrical signals are converted into output force or velocity, then we will have described the ability of the transducer to generate its acoustic output from the electrical signals. We can, for example, specify a transducer sensitivity as a ratio of an output (force or velocity) to an input (voltage or current). The specific sensitivity we will use is the ratio of the output velocity to the input current. Shown above is this sensitivity in terms of the transfer matrix components.

## Slide 20
Sensitivity, Impedance
All the other sensitivities can be found from this sensitivity if the transducer electrical impedance and acoustic radiation impedance are known:
A
Notes: Our choice of sensitivity was arbitrary but any other transducer sensitivity we might want to define can be obtained from this one (and the electrical and acoustic impedances) so this particular choice is all we need.

## Slide 21
A
Sensitivity, Impedance
Thus, we can replace the transfer matrix model of the transducer by a model consisting of an electrical impedance and an ideal "converter" that is defined by the transducer sensitivity:
Notes: If we know the electrical impedance and sensitivity we can bypass knowing the 2x2 transfer matrix components and simply and completely model the sending transducer as this impedance and sensitivity combination. Later, we will show that like the electrical impedance of the transducer we can easily measure its sensitivity with purely electrical measurements.

## Slide 22
Entire Sound Generation Process
transmitting
transducer
cable
pulser
output
force
Thevenin
input voltage
A
pulser
cable
transducer
sound generation
transfer function
=
=
Notes: We now can combine our pulser, cabling, and sending transducer models together and combine all these components into a single sound generation transfer function.

## Slide 23
Entire Sound Generation Process
transmitting
transducer
cable
pulser
output
force
Thevenin
input voltage
A
sound generation
transfer function
cable transfer function component(s)
Notes: Here is the explicit expression for this sound generation transfer function in terms quantities that are all either known or obtainable with electrical measurements.

## Slide 24
References
Ristic, V.M., Principles of Acoustic Devices, John Wiley, 1983
Kino. G.S., Acoustic Waves - Devices, Imaging and Analog
Signal Processing, Prentice-Hall, 1987.
Auld, B.A., Acoustic Fields and Waves in Solids, 2nd Ed.,
Vols. I and II, Krieger Publishing Co. , 1990.
Sacshe, W., and N.N. Hsu,” Ultrasonic transducers for materials
testing and their characterization,” in Physical Acoustics, Vol. XIV,
Eds. W.P. Mason and R.N. Thurston, 277-406, 1979.
Greeenspan, M., “Piston radiator: some extension of the theory,”
J. Acoust. Soc. Am., 65, 608-621, 1979.
Notes: Some references that explicitly deal with transducers.