## Slide 1
The Fast Fourier Transform (FFT)
and MATLAB Examples
Notes: In practice, Fourier transforms are calculated with a specific numerical procedure called a fast Fourier transform (FFT) so these slides will describe in detail how those calculations are performed, using MATLAB to illustrate specific examples.

## Slide 2
Learning Objectives
Discrete Fourier transforms (DFTs) and their relationship
to the Fourier transforms
Implementation issues with the DFT via the FFT
sampling issues (Nyquist criterion)
resolution in the frequency domain (zero padding)
neglect of negative frequency components
Notes: We will examine discrete Fourier transforms and their connections to the Fourier transform and show how discrete Fourier transforms are calculated with the fast Fourier transform algorithm. Various FFT implementation issues will be discussed.

## Slide 3
These Fourier integral pairs normally are performed
numerically by sampling the time and frequency
domain functions at discrete values of time and
frequency and then using the discrete Fourier transforms
to relate the sampled values
Notes: If ultrasonic signals are sampled, then instead of performing these Fourier integrals we need to perform sums of sampled values. These sums define the discrete Fourier transforms.

## Slide 4
Fast Fourier Transform
Discrete Fourier Transform
… time window sampled with N points
… sampling time interval
Notes: These are the discrete Fourier transform and its inverse which arise from sampling the Fourier integrals we defined earlier.

## Slide 5
As with the Fourier transforms, there are different choices
made for the Discrete Fourier transform pairs. In general, we
could write:
as long as
The indexing could also go from
1 to N instead of 0 to N-1
Fast Fourier Transform
Notes: The exact form of the discrete Fourier transform pairs, like the Fourier transform integrals, depend on the specific form we choose for those transforms. Note that these represent periodic functions while our ultrasonic signals are typically aperiodic. We have placed a p subscript on these quantities to indicate this periodicity. We will see that we must satisfy certain conditions to ensure this periodicity does not affect the calculations.

## Slide 6
These discrete Fourier Transforms can be implemented
rapidly with the Fast Fourier Transform (FFT) algorithm
Fast Fourier Transform
FFTs are most efficient if the number of samples, N, is
a power of 2. Some FFT software implementations require this.
N | (N-1)2 | (N/2)log2N
256 | 65,025 | 1,024
1,024 | 1,046,529 | 5,120
4,096 | 16,769,025 | 24,576
number of multiplications
direct calculation with the FFT
Notes: Performing these discrete Fourier transforms directly is computationally intensive but if we use a particular algorithm, called the fast Fourier transform (FFT) the number of multiplications can be drastically reduced as shown in the table. We will not describe the details of an FFT algorithm but there are many references available that do give that information. Note that some FFT algorithms require the number of sampled values be a power of 2 since that choice typically makes the algorithm more efficient.

## Slide 7
Mathematica
Fourier[{a1,a2,…,aN}]
InverseFourier[{b1,b2,…,bN}]
lists
Maple
FFT(N, xre, xim)
N = 2n
iFFT(N,Xre,Xim)
MATLAB
arrays
fft(x)
ifft(X)
arrays
Fast Fourier Transform
Notes: Different software packages implement the FFT in different forms. Here are some of the common cases.

## Slide 8
FFT function
Fast Fourier Transform
function y = FourierT(x, dt)
% FourierT(x,dt) computes forward FFT of x with sampling time interval dt
% FourierT approximates the Fourier transform where the integrand of the
% transform is x*exp(2*pi*i*f*t)
% For NDE applications the frequency components are normally in MHz,
% dt in microseconds
[nr, nc] = size(x);
if nr == 1
N = nc;
else
N = nr;
end
y = N*dt*ifft(x);
Notes: We will use the MATLAB functions (fft and ifft) to define new functions (FourierT and IFourierT) that are compatible with our definitions of the Fourier and discrete Fourier transforms and there inverses. Here is our FFT function FourierT.

## Slide 9
inverse FFT function
Fast Fourier Transform
function y = IFourierT(x, dt)
% IFourierT(x,dt) computes the inverse FFT of x, for a sampling time interval dt
% IFourierT assumes the integrand of the inverse transform is given by
% x*exp(-2*pi*i*f*t)
% The first half of the sampled values of x are the spectral components for
% positive frequencies ranging from 0 to the Nyquist frequency 1/(2*dt)
% The second half of the sampled values are the spectral components for
% the corresponding negative frequencies. If these negative frequency
% values are set equal to zero then to recover the inverse FFT of x we must
% replace x(1) by x(1)/2 and then compute 2*real(IFourierT(x,dt))
[nr,nc] = size(x);
if nr == 1
N = nc;
else
N = nr;
end
y =(1/(N*dt))*fft(x);
Notes: Here is our inverse FFT function IFourierT

## Slide 10
if
Nyquist
criterion
T
-T
tmax
fs
-fs
fmax
vp(t)
| Vp(f) |
N samples
N samples
Fast Fourier Transform
vp and Vp in the discrete Fourier transforms are periodic functions.
How do we guarantee these represent non-periodic pulses?
Notes: Shown here is a typical transient (aperiodic) ultrasonic signal and its spectrum, both repeated periodically. As long as the total time, T, of the sample window exceeds the time duration of the signal, and the sampling frequency is twice the maximum frequency present in the spectrum of the signal, then there is no overlap and we will obtain faithful representation of our signals in both the time and frequency domain, as shown. The condition that must be met on the sampling frequency is called the Nyquist criterion. In ultrasonic tests the frequencies involved typically are less than 20 MHz because of the transducers used and that fact that material attenuation also removes higher frequencies so one often samples ultrasonic NDE signals at a 100MHz sampling frequency, which is a very conservative choice satisfying the Nyquist criterion. Note that in the frequency domain the sampled spectrum values at negative frequencies are contained in the upper half of the sampled frequency domain values.

## Slide 11
The use of linspace and s_space functions for FFTs
and inverse FFTs
T =1.0
In the example above N = 8, T = 1.0 so
>> t = linspace(0,1, 8);
>> dt = t(2) -t(1)
dt = 0.1429
signal
periodically
repeated signal
Notes: In modeling our sampled ultrasonic signals we cannot use the built-in MATLAB function linspace as it does not generate the proper samples. To illustrate, consider this simple time domain function which is sampled over a time window T=1 with N = 8 samples so we want the sampling interval to be 1/8 and the sampled values to be the ones shown as red dots. If we use linspace( 0, 1, 8) we see an incorrect sampling interval (and the actual time values (not shown) will be incorrect)

## Slide 12
To get the proper sampled values and the correct Dt we must use the alternate function s_space (defined later)
>> t = s_space(0,1, 8);
>> dt = t(2)-t(1)
dt = 0.1250
>> t = linspace(0,1, 512);
>> dt = t(2) - t(1)
dt = 0.0020
>> t = s_space(0,1, 512);
>> dt = t(2) - t(1)
dt = 0.0020
Notes: We have defined a new MATLAB function, s_space, that generates the proper values, as shown above for our previous example. Note that if the number of sample points is large, then these differences between linspace and s_space are not as apparent, as we can see if we make N = 512. However, those differences are still present (see the next slide) so in generating sampled time and frequency domain functions we will always use s_space rather than linspace.

## Slide 13
When you are using many points the difference is not large if we use either linspace or s_space but the difference is still there
>> format long
>> t = linspace(0, 1, 500);
>> dt = t(2) -t(1)
dt = 0.00200400801603
>> t = s_space(0, 1, 500);
>> dt = t(2) -t(1)
dt = 0.00200000000000
Notes: If we use the Matlab command format long we can see the small differences between the use of s_space and linspace

## Slide 14
function y = s_space(xstart, xend, num)
% S_SPACE(XSTART,XEND, NUM) generates num evenly spaced sampled
% values from xstart to (xend - dx), where dx is the sample
% spacing. This is useful in FFT analysis where we generate
% sampled periodic functions. Example: generate 1000
% sampled frequencies from 0 to 100MHz via f =s_space(0,100,1000);
% In this case the last value of f will be 99.9 MHz and the
% sampling interval will be 100/1000 =0.1 MHz.
ye =linspace(xstart, xend, num+1);
y=ye(1:num);
Notes: Here is the s-space function which we see is a simple modification of the use of linspace to get the proper sampled values and sampling interval.

## Slide 15
>> load FBH_flaw_n8
>> size(texp)
ans =
1 1000
>> size(vexp)
ans =
1 1000
>> plot(texp, vexp)
>> dt = texp(2) - texp(1)
dt =
0.0100
>> fs = 1/dt
fs =
100.0000
>> vf = FourierT(vexp, dt);
>> f = s_space(0, fs, 1000);
>> plot(f, abs(vf))
72
74
76
78
80
82
84
-0.02
-0.015
-0.01
-0.005
0
0.005
0.01
0.015
0.02
0
10
20
30
40
50
60
70
80
90
100
0
0.5
1
1.5
2
2.5
3
3.5
x 10
-3
time values
voltage values
sampling interval
sampling frequency
flat-bottom hole
signal
Example of use of FourierT on a real ultrasonic signal
msec
MHz
Notes: Here is an example of Fourier analysis of an actual ultrasonic signal, which in this case is the signal reflected from a flat-bottom hole in a metal sample( a common reference reflector used in NDE).
The sampled voltage versus time signal is stored in a vector, vexp, and the sampled times are in the vector texp, both of which are loaded from a saved file into MATLAB. If we examine those vectors we see there are 1000 sampled time and voltage values and the sampling interval is 0.01 (microseconds) and the sampling frequency is 100 (MHz). The received time domain waveform is plotted.
If we do the FFT with our MATLAB function FourierT, we must generate a proper set of 1000 frequencies with s-space, after which we can plot the magnitude of the spectrum. We see most of the spectrum is between zero and 10 MHz and we see the corresponding negative frequency components in the upper half of the spectrum. Clearly our sampling frequency was more than sufficient in this case to satisfy the Nyquist criterion.

## Slide 16
>> plot(f(1:200), abs(vf(1:200)))
>>
0
2
4
6
8
10
12
14
16
18
20
0
0.5
1
1.5
2
2.5
3
3.5
x 10
-3
0
2
4
6
8
10
12
14
16
18
20
-4
-3
-2
-1
0
1
2
3
4
>> plot(f(1:200), angle(vf(1:200)))
magnitude of the spectrum
phase of the spectrum (in rad)
MHz
MHz
Notes: Here we see both the magnitude and phase of the frequency spectrum on a reduced frequency scale. Below 1 MHz and above 8 MHz the spectrum is small so that likely the phase values are contaminated by noise at those frequencies. We see that even in the 1-8 MHz range the phase is rapidly changing. We will examine the reason for this shortly.

## Slide 17
>> vt =IFourierT(vf, dt);
>> plot(texp, vt)
Warning: Imaginary parts of complex X and/or Y arguments ignored
>> plot(texp, real(vt))
72
74
76
78
80
82
84
-0.02
-0.015
-0.01
-0.005
0
0.005
0.01
0.015
0.02
inverse FFT
72
74
76
78
80
82
84
-0.02
-0.015
-0.01
-0.005
0
0.005
0.01
0.015
0.02
original signal
obtained from inverse FFT
msec
msec
Notes: Here we attempt to perform the inverse FFT with the MATLAB function IFourierT to recover our original time domain signal vt. We see that MATLAB gives us a warning that the signal has imaginary parts. These arise because there are always very small round-off errors in doing the complex arithmetic with these transforms, leaving some inconsequential imaginary values. We can remove those values by simply taking the real part of the signal which does recover our original signal.

## Slide 18
72
74
76
78
80
82
84
-0.02
-0.015
-0.01
-0.005
0
0.005
0.01
0.015
0.02
>> vshift =[ vexp(400:1000) vexp(1:399)];
>> plot (texp, vshift)
72
74
76
78
80
82
84
-0.02
-0.015
-0.01
-0.005
0
0.005
0.01
0.015
0.02
original time signal
shifted time signal
msec
msec
Notes: We saw previously that our signal had a rapidly changing phase. This was due to the fact that the signal was shifted in time to near the center of the plot. If move the signal closer to the left by moving the first 399 points in the beginning of the plot to the end of the plot then we obtain the shifted signal shown.

## Slide 19
>> vfs = FourierT(vshift, dt);
>> plot( f(1:200), abs(vfs(1:200)))
>> plot( f(1:200), angle(vfs(1:200)))
0
2
4
6
8
10
12
14
16
18
20
0
0.5
1
1.5
2
2.5
3
3.5
x 10
-3
0
2
4
6
8
10
12
14
16
18
20
-4
-3
-2
-1
0
1
2
3
4
same magnitude of spectrum as before
The phase is now different. This is to be
expected because recall a time delay
causes the spectrum to change only in
its phase, i.e.
MHz
MHz
Notes: If we now do an FFT of the shifted signal and plot the magnitude and phase of the spectrum over the first 200 points (going from 0 to 20 MHz) we see that the phase is less oscillatory because time delays produce a complex exponential term which affects the phase (but not the magnitude) of the spectrum, as seen above. If we move the signal even further to the left the oscillations will be even less than seen here.

## Slide 20
T
v (t)
N samples
2T
v (t)
2N samples
fs = 1/Dt
| V (f) |
N samples
Df
Df =1/T
Dt
fs = 1/Dt
| V (f) |
2N samples
Dt
Df =1/2T
Df
zero “padding”
Fast Fourier Transform
Notes: In some cases the sampling time interval (and hence the sampling frequency) may be adequate to prevent aliasing but we would like to increase the number of samples in the frequency domain to better capture any rapidly changing behavior there. We can do this by simply adding (padding) the time domain with zeros spaced at the same sampling time interval. Thus, the sampling frequency is not changed but the number of samples in the frequency domain will be larger. Shown above is an example where we pad a signal with N samples with N additional zeros and hence also double the number of samples in the frequency domain from N to 2N over the same frequency range. This is called zero padding.

## Slide 21
>> t =s_space(0, 4, 16);
>> v = t.*(t < 0.5) + (1-t).*(t >= 0.5 & t<=1.0);
>> h = plot(t, v, 'ko');
>> set(h, 'MarkerFaceColor', 'k')
>> axis([ 0 4 0 0.6])
>> dt = t(2) - t(1)
dt = 0.2500
0
0.5
1
1.5
2
2.5
3
3.5
4
0
0.1
0.2
0.3
0.4
0.5
Zero padding example
msec
Notes: As an example, here we generate samples of a triangular time domain function with s-space going from t =0 to t = 4 microseconds. Thus, the sampling interval is 4/16 = ¼ microseconds and the sampling frequency is 4 MHz. Note that s-space properly gives us the correct 16 points and those points do not include a point at t = 4 microseconds as that point is the same as the one at t =0.

## Slide 22
>> f =s_space(0, 1/dt, 16);
>> vf = FourierT(v, dt);
>> h = plot(f, abs(vf), 'ko');
>>axis([ 0 4 0 0.3])
>> set(h, 'MarkerFaceColor', 'k')
>> df = f(2) - f(1)
df = 0.2500
0
0.5
1
1.5
2
2.5
3
3.5
4
0
0.05
0.1
0.15
0.2
0.25
MHz
Notes: If we compute the FFT of this sampled function and generate a set of sampled frequencies with s_space, then we obtain the 16 sampled frequency domain values as shown with the spacing of ¼ MHz. Note again s_space gives us the proper sampled values and that does not include a value at f = 4 MHz, which is the same as the value at f = 0.

## Slide 23
>> vt2 =[v, zeros(1,16)];
>> vf2 = FourierT(vt2, dt);
>> h = plot(f, abs(vf2), 'ko');
??? Error using ==> plot
Vectors must be the same lengths.
>> f =s_space(0, 1/dt, 32);
>> h = plot(f, abs(vf2), 'ko');
>> set(h, 'MarkerFaceColor', 'k')
>>axis([ 0 4 0 0.3])
could also use
vt2 = padarray(v,[0, 16], 0, ‘post’);
>> df=f(2) - f(1)
df = 0.1250
half the former df
same sampling frequency
Now, pad the original signal with zeros
0
0.5
1
1.5
2
2.5
3
3.5
4
0
0.05
0.1
0.15
0.2
0.25
MHz
Notes: Now, we pad our original time domain signal by adding 16 zeros and then do a FFT. If we try to plot the result we get an error because our set of frequency values has doubled so we must generate a new set of 32 frequencies from zero to the sampling frequency. Then the plot works fine and we see a much finer resolution where now the frequency domain sampling interval is 1/8 MHz.

## Slide 24
>> t =s_space(0, 4, 512);
>> v = t.*(t < 0.5) + (1-t).*(t >= 0.5 & t<=1.0);
>> dt = t(2) -t(1)
dt = 0.0078
>> fs =1/dt
fs = 128
>> f =s_space(0, fs, 512);
>> vf =FourierT(v, dt);
>> plot(f, abs(vf))
Now, use a much higher sampling frequency
0
20
40
60
80
100
120
140
0
0.05
0.1
0.15
0.2
0.25
MHz
Notes: We used the triangular function example to illustrate zero padding, using very few points so we could easily see the results. However, did we adequately address aliasing? To answer this let us use a much higher sampling frequency (128 MHz = 32 times higher than previously used) as shown here and plot the magnitude of the spectrum. We see in this case the positive and negative frequency values are well separated and the spectral values appear to be small below about 10 MHz. Let us examine those values on a smaller scale (next slide)

## Slide 25
>> h = plot(f(1:20), abs(vf(1:20)), 'ko');
>> set(h, 'MarkerFaceColor', 'k')
To see the frequency spectrum on a finer scale
0
1
2
3
4
5
0
0.05
0.1
0.15
0.2
0.25
Note: we had some aliasing before
MHz
Notes: If we plot the first 20 values of the spectrum (which are values from approximately 0 to 5 MHz) we see that there are some small higher frequency values that were missed previously so a sampling frequency of 4 MHz was not sufficient to completely prevent aliasing.

## Slide 26
We can do multiple FFTs or IFFTs
all at once if we place the data in columns
>> t =s_space(0, 4, 16);
>> v = t.*(t < 0.5) + (1-t).*(t >= 0.5 & t<=1.0);
>> dt = t(2) - t(1);
>> mv= [ v' v' v'];
>> mvf = FourierT(mv, dt);
>> vf1 = mvf(:,1);
>> f = s_space(0, 1/dt, 16);
>> h = plot(f, abs(vf1)', 'ko')
>> set(h, 'MarkerFaceColor', 'k')
0
0.5
1
1.5
2
2.5
3
3.5
4
0
0.05
0.1
0.15
0.2
0.25
MHz
Notes: Note that we can do multiple FFTs or inverse FFTs all at once for multiple signals if we place those sampled signals in a matrix where the sampled values are in the columns of that matrix. Here we generate such a matrix which simply contains the original triangular function used previously but duplicated three times in the columns of the matrix mv. We then do the FFT of that matrix and extract the first column of frequency domain values in the matrix mvf and plot them. Identical values are obviously contained in the other two columns.

## Slide 27
Note that even though there is aliasing here if we do the inverse FFT of these samples we do recover the original time samples:
>> v1 =IFourierT(vf1,dt);
>> h=plot(t, real(v1), 'ko');
>> set(h, 'MarkerFaceColor', 'k')
0
0.5
1
1.5
2
2.5
3
3.5
4
-0.1
0
0.1
0.2
0.3
0.4
0.5
0.6
msec
Notes: Recall that the sampling used in the previous slide was insufficient to prevent aliasing. In spite of that fact, when we perform an inverse FFT we do obtain the proper time domain function. Thus, aliasing generates incorrect frequency domain values through the FFT but does not prevent us from recovering the original function with the inverse FFT.

## Slide 28
Fast Fourier Transform
FFT Examples using the function:
function y = pulse_ref(A,F,N, t)
y = A*(1 -cos(2*pi*F*t./N)).*cos(2*pi*F*t).*(t >= 0 & t <= N/F);
A … controls the amplitude
F … controls the dominant frequency in the pulse
N … controls the number of cycles (amount of "ringing")
in the pulse and hence the bandwidth
MATLAB function:
Notes: Here, we will define a function that is controlled by three parameters (A, F, N) that will allow us to demonstrate some explicit results.

## Slide 29
>> t = s_space(0,5,512);
>> dt = t(2)- t(1)
dt = 0.0098
>> y=pulse_ref(1,5,3,t);
>> plot(t, y)
>> yf1=FourierT(y,dt);
>> f=s_space(0, 1/dt, 512);
>> f(end)
ans = 102.2000
>> plot(f, abs(yf1))
Frequency spectrum for relatively wideband pulse
if t is in msec
f is in MHz
sampling
frequency
Nyquist frequency
= ½ sampling
frequency
0
1
2
3
4
5
-2
-1
0
1
2
0
20
40
60
80
100
120
0
0.05
0.1
0.15
0.2
0.25
0.3
0.35
msec
MHz
Notes: If we let A =1 , f = 5 , N =3 we will generate a short signal with little ringing that has a relatively broad spectrum. As shown we will choose a sampling frequency of about 100 MHz which from the spectrum seen is vey conservative.

## Slide 30
>> plot(f(1:100), abs(yf1(1:100)))
Expanded view
0 – 20 MHz
0
2
4
6
8
10
12
14
16
18
20
0
0.05
0.1
0.15
0.2
0.25
0.3
0.35
0
0.5
1
1.5
2
2.5
3
3.5
4
4.5
5
-2
-1.5
-1
-0.5
0
0.5
1
1.5
2
msec
MHz
Notes: If we look at the spectrum on a finer scale we see a relatively broad spectrum centered at 5 MHz.

## Slide 31
>> y = pulse_ref(1,5,5,t);
>> yf2 = FourierT(y, dt);
>> plot(f(1:100), abs(yf2(1:100)))
Somewhat more
narrow band pulse
(only 0 - 20 MHz
shown)
0
0.5
1
1.5
2
2.5
3
3.5
4
4.5
5
-2
-1.5
-1
-0.5
0
0.5
1
1.5
2
0
2
4
6
8
10
12
14
16
18
20
0
0.1
0.2
0.3
0.4
0.5
msec
MHz
Notes: If we increase the amount of “ringing” in the signal by making N larger ( N =5) we see a somewhat narrower bandwidth for the spectrum.

## Slide 32
>> y = pulse_ref(1,5,10,t);
>> yf3 = FourierT(y, dt);
>> plot(f(1:100), abs(yf3(1:100)))
Decrease bandwidth
even more
(only 0 - 20 MHz
shown)
0
1
2
3
4
5
-2
-1
0
1
2
0
2
4
6
8
10
12
14
16
18
20
0
0.2
0.4
0.6
0.8
1
msec
MHz
Notes: If we increase the amount of ringing even more ( N = 10) we see an even narrower spectrum

## Slide 33
Df is not quite adequate here
Df =1/T = 1/5 MHz
>> plot(f(1:50), abs(yf3(1:50)))
Show plot in more detail
0
1
2
3
4
5
6
7
8
9
10
0
0.2
0.4
0.6
0.8
1
we can improve these results with zero padding of our signal
MHz
Notes: If we examine the spectrum of this narrowband signal on a finer scale we see that the spectrum is jagged, indicating that our spacing in the frequency domain is not adequate. We can use zero padding to improve the results, as we will now show.

## Slide 34
zero padding
now, have 1024 points over 10
microseconds, so dt is same but
T = Ndt is twice as large
0
1
2
3
4
5
6
7
8
9
10
-2
-1
0
1
2
>> t=s_space(0, 10, 1024);
>> y=pulse_ref(1, 5,10, t);
>> plot(t,y)
>> dt = t(2) -t(1)
dt = 0.0098
recall, originally, we had
t = s_space(0,5, 512);
we could also zero pad via
t = [t, zeros(1, 512)];
msec
Notes: Here we double the number of points with zero padding but keep the same sampling frequency.

## Slide 35
>> yf4 = FourierT(y, dt);
>> f = s_space(0, 1/dt, 1024);
>> plot(f(1:100), abs(yf4(1:100)))
Improved representation of the
spectrum Df = 1/T = 1/10 MHz
0
1
2
3
4
5
6
7
8
9
10
0
0.2
0.4
0.6
0.8
1
1.2
1.4
MHz
Notes: Now if we examine the spectrum we see a smoother signal. We can improve the results even more by adding more zeros.

## Slide 36
fs
fmax
| Vp(f) |
N samples
positive frequency
components
negative frequency
components
fs
fmax
| Vp(f) |
N samples
positive frequency
components
?
in time domain
if v(t) is real
Fast Fourier Transform
( )* = complex conjugate
Notes: When we perform an FFT we see that in the frequency domain we obtain the positive frequency components in the lower half of the spectrum and the negative frequency components in the upper half of the spectrum. The negative frequency values are just the complex conjugate of the positive frequency components so they do not contain any new information. They exist solely to guarantee that the original time domain signal was a real signal. What happens if we simply replace the negative frequency values by zeros and then do an inverse FFT?

## Slide 37
Hilbert transform of v(t)
so
Fast Fourier Transform
Notes: The answer is we obtain a complex signal where one half of our original time domain signal is in the real part and the imaginary part contains minus one half of the Hilbert transform of our original time domain signal. Thus, we can replace the upper half our spectrum by zeros and recover our original real time domain signal by just taking twice the real part of the inverse FFT of the remaining positive frequency components.

## Slide 38
>> t = s_space(0,5, 512);
>> y = pulse_ref(1,5,10,t);
>> plot(t, y)
>> yf= FourierT(y, dt);
>> yf5 = yf .*(f < 50);
>> plot(f, abs(yf5))
zero negative
frequency components
Zero out negative frequency components
now, do the inverse FFT
on just these positive
frequency components
(and zeros in the upper
half part of the spectrum)
0
1
2
3
4
5
-2
-1
0
1
2
0
20
40
60
80
100
120
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
1
msec
MHz
Notes: Here is an example where we compute the spectrum of signal and replace the negative frequency values by zeros. However, what about the zero frequency value in the spectrum? Do we consider it a positive or negative value? The answer is: we consider half of it positive and half of it negative so that we divide the zero frequency value of the spectrum (if it is non-zero) by two before we do an inverse FFT.

## Slide 39
>> yf5(1) = yf5(1)/2;
>> y = 2*real(IFourierT(yf5, dt));
>> plot(t, y)
when throwing out negative frequency
components, need to divide dc value
by half also (not needed if dc value is zero or
already very small but it is a good idea to always
do it)
0
1
2
3
4
5
-2
-1
0
1
2
0
1
2
3
4
5
-2
-1
0
1
2
original signal
recovered signal
from real frequency components
msec
msec
Notes: Here we see the zero frequency value being divided by two and then twice the real part of the inverse FFT is calculated. We see we do recover the original signal

## Slide 40
Homework Problems
A.1, A.2, S.0, S.1
Notes: Special homework problems and problems from Appendix A.

## Slide 41
References
Walker, J.S., Fast Fourier Transforms, CRC Press, 1996
Burrus, C.S. and T.W. Parks, DFT/FFT and Convolution
Algorithms, John Wiley and Sons, New York, 1985.
Fast Fourier Transform
Notes: There are many references on Fourier transforms and the fast Fourier transform. Here are several of them.