## Slide 1
Neural Networks
Notes: Neural networks have become an important and powerful tool for analyzing signals so they are a valuable concept that can be used to evaluate the results of ultrasonic NDE inspections.

## Slide 2
Learning Objectives
Characteristics of neural nets
Supervised learning – Back-propagation
Probabilistic nets
Notes: In the following slides we will give a very brief introduction to neural networks. We will discuss only two network types – a feedforward net trained with the back-propagation learning algorithm, and a probabilistic net. We made these two choices since the back-prop net is perhaps the most widely used network to describe the working of neural nets and the probabilistic net is closely related to the probabilistic ideas we discussed in the pattern recognition presentation.

## Slide 3
According to the DARPA Neural Network Study
(1988, AFCEA International Press, p. 60):
... a neural network is a system composed of many simple processing elements operating in parallel whose function is
determined by network structure, connection strengths, and the processing performed at computing elements or nodes.
What is a Neural Network?
Notes: Here is a formal definition of a neural network. Generally speaking, a neural net has many interconnected elements which work in unison to accomplish a particular task.

## Slide 4
Characteristics of Neural Nets
The good news: They exhibit some brain-like behaviors that are difficult to program directly like:
learning
association
categorization
generalization
feature extraction
optimization
noise immunity
The bad news: neural nets are:
black boxes
difficult to train in some cases
Notes: Neural nets have some very good characteristics but also some bad ones as well. The power exhibited by neural nets generally far outweigh their negative aspects.

## Slide 5
There is a wide range of neural network architectures:
Multi-Layer Perceptron (Back-Prop Nets) 1974-85
Neocognitron 1978-84
Adaptive Resonance Theory (ART) 1976-86
Sef-Organizing Map 1982
Hopfield 1982
Bi-directional Associative Memory 1985
Boltzmann/Cauchy Machine 1985
Counterpropagation 1986
Radial Basis Function 1988
Probabilistic Neural Network 1988
General Regression Neural Network 1991
Support Vector Machine 1995
Notes: Here we show a number of different neural nets developed in the 80s and 90s. We will only describe back-propagation nets and probabilistic nets, as mentioned earlier.

## Slide 6
class c1
class c2
Our single "neuron" model
Notes: Here is the model of a single “neuron” that implements the linearly separable classifier we discussed in the pattern recognition notes.

## Slide 7
Basic Neuron Model
sum
threshold
x1
x2
x3
xn
jth neuron
input features
and bias
wji
wj2
wj3
wjn
activation function
Notes: Here is a more general “neuron” model that takes a set of weighted inputs, sums those inputs, and then applies an “activation function” to that sum to determine an output.

## Slide 8
C1
C1
C1
C3
C2
C2
C2
C3
C3
output
hidden layer
output
output
input layer
hidden
layer 1
hidden
layer 2
Notes: We saw that with a single neuron we can generate a linearly separable classifier. By adding one or more layers we can generate a network of neurons that can handle more complex problems since the decision surfaces (discriminants) are not limited to a single hyperplane. These decision surfaces are defined by the weights in the connections between neurons so a key aspect is how we learn to choose those weights.

## Slide 9
Most neural nets use a smooth activation function
sum
threshold
x1
x2
x3
xn
input features
and bias
wji
wj2
wj3
wjn
a sigmoidal function
and its
derivative
Notes: Neural nets usually use a smooth activation function that we will see facilitates the determination of the network weights. A sigmoidal function is a popular choice.

## Slide 10
x
w
u
y
h
x
y
Major question – How do we adjust the weights to learn the mapping between inputs and outputs?
Answer: Use the back propagation algorithm, which is just an application of the chain rule of differential calculus.
Consider this simple example
Notes: The crucial question is how to determine the weights. A procedure, called the back propagation algorithm, allows us to answer that question. To see how back propagation works, consider a simple case of a set of three neurons connected together with unknown weights, w, u.

## Slide 11
To learn the weights we can try to minimize the output error
i.e. , we start with an initial guess for the weights and then present an example
of known input x and output value d (training example). Then we form up the error
and adjust the weights to reduce this error. Since
we can make
by choosing
… constant
Notes: To determine the weights we take an example where an input x determines a known output d and try to minimize the output error of the network on this example. We can make the error always smaller by making the derivatives of the error function with respect to the weights proportional to the change of weights themselves as shown.

## Slide 12
This leads to the adjustment rule
So we now need to find these derivatives of E with respect to the weights.
… learning
rate
Notes: This can be written as a rule for changing the weights in terms of the derivatives of the error.

## Slide 13
x
w
u
y
h
x
y
For the derivatives involving the weight between the hidden layer and output layer
Notes: Since the relationship between the network output and input is just a composite function, we can obtain the error derivatives explicitly as shown here for one error derivative, ∂E/∂u (the expression for the derivative shown earlier for the sigmoidal function is used here). Choosing a smooth function like the sigmoid allows us to compute these derivatives.

## Slide 14
Similarly for the weight between the hidden layer and input layer
Notes: Here is the other error derivative. Thus, we are really just applying the chain rule of Calculus in this backpropagation algorithm.

## Slide 15
Thus, the training algorithm is:
1. Initialize weights to small random values
2. Using a training set of known pairs of inputs and outputs (x, d) change the weights according to
with
until
becomes sufficiently small
E
stop
iteration
This is an example of supervised learning
Notes: Thus, we now know how to use a set of known examples of input/output combinations (called a training set) to change the weights to minimize the output error. Once the error is small enough, we can say the neural network has been trained. This is called supervised learning.

## Slide 16
hidden layer
outputs
One of the most popular neural nets is a feed forward net with one hidden layer trained by the back propagation algorithm
It can be shown that in principle this type of network can represent an arbitrary input-output mapping or solve an arbitrary
classification problem
Notes: Now, consider a feed forward network with a hidden layer.

## Slide 17
Back propagation algorithm (three layer feed forward network)
P input
nodes
M hidden
nodes
K output
nodes
with
yk
xi
Notes: We can apply the same backpropagation algorithm to train this neural network.

## Slide 18
Some issues associated with this "back-prop" network
design of training, testing and validation data sets
determination of the network structure
selection of the learning rate (m)
problems with under or over-training
E
iterations
training set
testing set
stop
learning
over
trained
Notes: Here are some of the questions that occur with such training of such “back-prop neural nets”. For example, how do we choose sets of training examples and examples to validate the performance? Also, how do we choose the actual network architecture (number of nodes, layers)? There is a learning rate, μ , in the backpropagation algorithm, that also must be chosen. Also, we need to determine when to stop the training since we may make the error of the network on the training examples be very small, but a smaller training error does not always mean a better performance of the network on other examples, as we may simply have trained the network to only recognize the testing examples very well.

## Slide 19
Some important issues for neural networks:
Pre-processing the data to provide:
reduction of data dimensionality
noise filtering or suppression
enhancement
strengthening of relevant features
centering data within a sensory aperture or window
scanning a window over the data
invariance in the measurement space to:
translations
rotations
scale changes
distortion
data preparation
analog to digital conversion
data scaling
data normalization
thresholding
Notes: Here are some issues of preprocessing the input data (training examples) that might be useful.

## Slide 20
Some examples of pre-processing include
1-D and 2-D FFTs
Filtering
Convolution Kernels
Correlation Masks or Template Matching
Autocorrelation
Edge Detection and Enhancement
Morphological Image Processing
Fourier Descriptors
Walsh, Hadamard, Cosine, Hartley, Hotelling, Hough Transforms
Higher order spectra
Homomorphic Transformations (e.g. Cepstrums)
Time-Frequency transforms ( Wavelet, Wigner-Ville, Zak)
Linear Predictive Coding
Principal Component Analysis
Independent Component Analysis
Geometric Moments
Thresholding
Data Sampling
Scanning
Notes: Here are some explicit pre-processing steps. A feedforward neural network trained with the back propagation algorithm used in conjunction with such steps can be a very powerful tool.

## Slide 21
Probabilistic Neural Network (PNN)
Basic idea:
Use training samples themselves to obtain a representation of the probability distributions for each class and then use Bayes decision rule to make a classification
Basis functions usually chosen are Gaussians:
i … class number (i = 1, 2, …, N)
j … training pattern number
xij … j th training pattern from i th class
Mi … number of training vectors in class i
p .. dimension of vector x
fi (x) = sum of Gaussians centered at each training pattern from the ith class to represent the probability density of that class
s … smoothing factor (standard deviation, width of the Gaussians)
Notes: Here is another neural network, called a probabilistic neural net, that uses the samples (training examples) directly to define the probability distributions for a set of output classes and then applies Bayes decision rule to make a classification. Gaussian functions are often used, as shown here.

## Slide 22
probability density function for class i
If we normalize the vectors x and xij to unit length and assume the number of training samples from each class are in proportion to their a priori probability of occurrence then we can take as our decision functions
Notes: Here are the decision functions that can be defined from the training a samples.

## Slide 23
Since we decide for a given class k based on
for all
the common constant outside the sum makes no difference and we can take
This can now be easily implemented in a neural network form
Notes: Then we simply choose the largest decision function to make a classification decision.

## Slide 24
x1
xj
xp
1
M1
1
1
Mi
MN
Probabilistic Neural Network
weights are
just elements of the training
patterns
xij
Notes: This whole process can be structures as a neural network where the weights are now simply the known elements of the training examples.

## Slide 25
Characteristics of the PNN
1. no training, weights are just the training vectors themselves
2. only parameter that needs to be found is the smoothing factor, s
3. outputs are representative of probabilities of each class directly
4. the decision surfaces are guaranteed to approach the Bayes optimal boundaries as the number of training samples grows
5. "outliers" are tolerated
6. sparse samples are adequate for good network performance
7. can update the network as new training samples become available
8. needs to store all the training samples, requiring a large memory
9. testing can be slower than with other nets
Notes: Here are some of the properties of the probabilistic neural network. We see that it is a nice illustration of the probabilistic pattern recognition ideas we presented earlier in a neural network form.

## Slide 26
References
Specht, D.F., " Probabilistic neural networks," Neural Networks, 3, 109-118, 1990.
Haykin, S., Neural Networks, a Comprehensive Foundation, 2nd Ed., Prentice-Hall, 1999.
Haykin, S., Neural Networks and Learning Machines, 3rd Ed., Pearson, 2016.
Bishop, C.M., Neural Networks for Pattern Recognition, Clarendon Press, 1995.
Bishop, C.M., Pattern Recognition and Machine Learning, Springer, 2006.
Geron, A., Hands-on Machine Learning with SciKit-Learn, Keras, and TensorFlow, 2nd Ed., O Reilly Media, 2019.
Notes: Here are a few references that contain more information on back-prop nets and probabilistic nets, as well as others.