## Slide 1
Transducer Sound Radiation
Notes: An important part of the acoustic/elastic transfer function are the waves generated by an ultrasonic transducer. We will describe those waves here.

## Slide 2
Learning Objectives
Planar Immersion Transducer
on-axis near field - far field
radiation into solid-normal incidence, plane interface
diffraction correction
Spherically focused transducer
on axis field
focal spot size
radiation into solid-normal incidence, plane interface
diffraction correction
Notes: We will examine with models some of the basic characteristics of the wave fields generated with planar and spherically focused immersion transducers.

## Slide 3
Learning Objectives (continued)
Contact P-wave transducer on a solid
wave types present
directivity functions
Angle beam shear wave transducer
Overview of beam theories
Notes: We will also examine the wave fields of other types of transducers such as contact and angle beam transducers and give a brief summary of the types of theories that are available to model transducers.

## Slide 4
Ultrasonic Beam Models
Planar transducer radiating into a fluid
z,z'
x,x'
y,y'
r
x = (x,y,z)
y = (x',y',z' = 0)
dS
vz
infinite baffle
Can show that each area element that is in
motion acts like a source of spherical waves:
Notes: First, consider a planar (unfocused) immersion transducer radiating into a fluid. We will model the transducer ( in the frequency domain) by assuming that there is a velocity field acting normal to the transducer face over the surface, S, of its face and that the rest of the plane is motionless (called a rigid baffle). If we examine a small element, dS, of that surface, we can show that this element acts like a point source and radiates a spherical wave and generates a small pressure, dp, which is shown.

## Slide 5
If we let vz(x',y',w) = v0(w) (piston model)
Adding up all such sources over the face of the transducer gives
the Rayleigh-Sommerfeld Integral
Notes: If we add up all such spherical waves then the total pressure at any point in the fluid is given by the Rayleigh-Sommerfeld integral (also called the Rayleigh integral). For a piston transducer this integral becomes the simpler form shown. In this form we are simply adding up ( in integral form) spherical waves originating the face of the transducer.

## Slide 6
Note: horizontal axis scale is much larger than vertical axis scale
plot of the magnitude of the pressure for a 5 MHz, 0.5 inch diameter transducer radiating into water
Notes: If we numerically evaluate the Rayleigh-Sommerfeld integral for a 5 MHz, 0.5 inch diameter immersion transducer, we can show a cross-sectional plot of the pressure wave field, where red indicates high pressure and blue is low pressure. We see that close to the transducer there is a complex field and that overall the wave field is well collimated, i.e. it is contained mostly in a cylindrical region extending into the fluid from the transducer face. Note that what we are seeing here is the pressure in the frequency domain at a frequency of 5 MHz. A real transducer puts out a pulse of sound but if we compute the FFT of a piston transducer where the velocity on its face is a delta function in time and examine the 5 MHz component of that response at all points in the wave field, we obtain this result.

## Slide 7
For on-axis response of a circular transducer of radius, a
a
r
z
x
y
It can be shown that
the area element can be
written as dS = r dr df
direct wave
edge wave
Notes: For points in the fluid along the central axis of the transducer we can integrate the Rayleigh-Sommerfeld integral and obtain an explicit expression for the on-axis pressure. That expression has two terms which we can identify as a direct wave from the face of the transducer and a wave that has come from the edge of the transducer face.

## Slide 8
direct wave
edge wave
edge wave
baffle
Direct and edge waves as seen for a pulsed piston transducer
Notes: If we examine the full wave field of the transducer we can show that the direct wave is actually a plane wave that exists only within a cylinder that extends from the transducer face while the edge wave is in the form of a wave that appears to originate from the edge of the transducer and in 3-d looks like a half “donut” in shape.

## Slide 9
0
0.5
1
1.5
2
2.5
3
3.5
4
0
0.2
0.4
0.6
0.8
1
1.2
1.4
1.6
1.8
2
z/N
Approximate Near field distance N = a2/l
Maxima: z = N/(2m+1) m = 0,1,2,…
Minima: z = N/2n n = 1,2,3,...
a = 6.35 mm
f= 5 MHz
c = 1500 m/s
|p|
rcv0
Example: for a 5 MHz,
1/2 in. diameter transducer radiating into water
N = 5 in. (approx.)
on-axis pressure:
Notes: If we plot the magnitude of the on-axis pressure we see that for distance less than a near field distance, N, there are successive maxima and minima in the pressure. This is called the near field of the transducer. At about three near field distances or greater the pressure simply decays like 1/z in magnitude, which is the characteristic decay seen for a point source. This makes sense since sufficiently far from the transducer we expect the whole transducer itself will appear as a small point-like source. This region z > 3N is called the far field region of the transducer. We will say more about the far field later.

## Slide 10
Paraxial approximation : a/z <<1
z
a
plane wave
C1(a,w,z)
diffraction coefficient
on-axis pressure:
Notes: If we assume that we are not too close to the transducer so that we can assume a/z <<1 (note this does NOT assume we are in the far field) then we can use this so-called paraxial approximation to write the on-axis pressure as simply a plane wave multiplied by a correction factor called a diffraction coefficient. Thus, in the paraxial approximation we can treat the on-axis wave field as a quasi-plane wave. Basically, the paraxial approximation assumes the waves are all approximately traveling in the z-direction. From our previous cross-sectional view where we saw the pressure wavefield was well-collimated we can expect the paraxial approximation can be used also for off-axis points, not just the on-axis points seen here.

## Slide 11
0
0.5
1
1.5
2
2.5
3
3.5
4
0
0.2
0.4
0.6
0.8
1
1.2
1.4
1.6
1.8
2
z/N
0
0.5
1
1.5
2
2.5
3
3.5
4
0
0.2
0.4
0.6
0.8
1
1.2
1.4
1.6
1.8
2
z/N
exact result
paraxial result
|p|
rcv0
|p|
rcv0
on-axis pressure:
Notes: Here we can compare the exact on-axis pressure with the paraxial approximation result, showing we capture both the near field and far field behavior well with the paraxial approximation. Generally, the paraxial approximation is valid if we are greater than about a transducer diameter away from its face.

## Slide 12
function p = on_axis(zN, A,c,F)
% exact on axis pressure from a piston source
%radiating into a fluid. A is radius in mm, c the
%wavespeed of the fluid in m/sec, F the frequency in MHz,
% zN is the distance in the fluid divided by the near field
%distance a^2/lamba (lamba is the wavelength)
al= 1000*A*F/c; % a/lamba
ka = 2*pi*al; % ka for the transducer
kz = ka*al*zN;
ke = 2*pi*(al^2).*sqrt(zN.^2 + (1/al)^2);
p = exp(i*kz) - exp(i*ke);
Notes: Here is the MATLAB code for calculating the exact on-axis pressure.

## Slide 13
function p = par_on_axis(zN, A,c,F)
% paraxial axis pressure from a piston source
%radiating into a fluid. A is radius in mm, c the
%wavespeed of the fluid in m/sec, F the frequency in MHz,
% zN is the distance in the fluid divided by the near field
%distance a^2/lamba
al= 1000*A*F/c; % a/lamba
ka = 2*pi*al; % ka for the transducer
kz = ka*al*zN;
ke = ka./(2*al.*zN);
p = exp(i*kz).*(1 - exp(i*ke));
Notes: Here is the MATLAB code for calculating the on-axis pressure in the paraxial approximation.

## Slide 14
MAT> z = linspace(.2, 4,500);
MAT> p = on_axis(z,6.35,1500,5);
MAT> plot(z, abs(p))
MAT> xlabel('z/N')
MAT> p = par_on_axis(z, 6.35, 1500, 5);
MAT> plot(z, abs(p))
MAT> xlabel('z/N')
Notes: Here is the MATLAB code for generating the on-axis comparison plots we have just seen.

## Slide 15
On-axis response at normal incidence to a plane interface
(paraxial approximation)
z1
z2
fluid
solid
dp
transmission coefficient
(at normal incidence)
(velocity/velocity)
same diffraction correction
expression as for a single fluid
displacement
x
velocity in
the solid
Notes: Since the wave field of the transducer behaves like a quasi-plane wave in the paraxial approximation, we can use plane wave theory and obtain the wave field in more complex situations such as where an immersion transducer radiates a compressional wave into a solid, where the transducer is at normal incidence to a plane fluid-solid interface. In this case we can write the velocity field as that of a plane wave that has traveled in the fluid and across the plane interface multiplied by a diffraction correction. In this case we can show that the diffraction coefficient is the same as that for the single fluid problem where the distance z is replaced by the equivalent distance shown.

## Slide 16
z1
z2
a
d1
d2
x
d
"virtual" point where the edge
wave would arrive on-axis in the solid if cp2 = cp1
e
so
which gives, in the paraxial approximation
qp1
qp1
qp2
Notes: We can give a physical interpretation of the equivalent distance by examining a wave that arrives on the axis from transducer edge. Using the geometry, Snell’s law, and the paraxial approximation, we see that the equivalent distance is just the distance along the axis the edge wave would travel if it had simply been propagating in a single medium.

## Slide 17
S
x
y
r
R
y =(x,y,0)
e
The far-field is usually defined as z > 3N - also
called the "spherical wave region"
Far-field beam of a planar piston transducer
Notes: Here we will examine the far field region of a piston transducer in more detail. We will see that we can get explicit results for the pressure anywhere, not just on axis. We can examine the radius, r, from a point on the transducer face to a general point in the fluid and approximate that distance in terms of the radius, R, from the center of the transducer and the unit vector, e, which defines the direction to the point in the fluid. As a function of R, we see the behavior exp(ikR)/R is just that of a spherical wave so in the far field the wavefield of the transducer behaves like a spherical wave whose angular dependency is governed by the remaining integral . The remaining integral is one we can perform in a number of cases.

## Slide 18
Define the 2-D spatial Fourier
transform of Q , where
as
Then the far field pressure can be written as
angular beam profile
spherical wave
Notes: The remaining integral can be expressed as a 2-D Fourier transform, F, of a characteristic function,  , which is just equal to one on the plane of the transducer face and zero outside that face. This integral gives us the angular beam profile.

## Slide 19
a
b
x
y
q
f
In spherical coordinates
Rectangular Piston Transducer
z
Notes: Here is the expression for the angular beam profile of a rectangular transducer in terms of spherical angles.

## Slide 20
Example far-field pattern of a rectangular transducer
-6
-4
-2
0
2
4
6
-10
-5
0
5
10
x-axis distance
y-axis distance
a = 3 mm in y-direction , b = 6 mm in x-direction
R = 70 mm, f = 5 MHz.
Notes: If we make a contour plot of the angular beam profile in a plane parallel to the transducer face in the far field we see a central lobe and multiple side lobes

## Slide 21
Circular Piston Transducer
a
q
|p|
rcv0
z = 3N
z = 6N
-150
-100
-50
0
50
100
150
0
0.2
0.4
0.6
0.8
1
1.2
1.4
radial distance, mm
z
r
R
r
Notes: Similarly for a circular piston transducer we can obtain the angular beam profile in terms of a Bessel function. Here, we plot the magnitude of the pressure at both three and six near field distances from the transducer, showing how the main lobe of the transducer and the side lobes spread as we get further from the transducer and , of course, the amplitude gets smaller due to the spherical spreading term

## Slide 22
MAT> ang = linspace(-10, 10,500);
MAT> [p,r] =far_field(ang,6.35,1500,5,3);
MAT> plot(r,abs(p), '--')
MAT> hold on
MAT> [p,r] =far_field(ang,6.35,1500,5,6);
MAT> plot(r,abs(p), 'red')
MAT> xlabel('radial distance, mm')
function [p, rho] = far_field(ang,A, c, F, RN)
% far_field computes the normalized far field pressure
% for a circular piston (omitting the exp(ikR) phase term)
% A is the radius of the transducer in mm, c the wavespeed
%in m/sec, F the frequency in MHz, and RN is
%the normalized radial distance in near field units.
% rho is the transverse distance (normal to z) in mm
ka = 2*pi*(1000*A*F/c);
al= 1000*A*F/c;
x = ka*sin(ang*pi/180);
rho =RN*(A*al)*sin(ang*pi/180);
p = -i*(ka/(al*RN))*besselj(1,x)./(x+eps*(x ==0));
Notes: Here is the MATLAB code for obtaining the plots on the previous page.

## Slide 23
Spherically Focused Piston Transducer Radiating
Into a Fluid
O’Neil Model
uniform
velocity, v0
Sf ... spherical surface
a
R0
Notes: A real spherically focused transducer is made by placing an acoustic lens on the face of the transducer. However, O’Neil has shown we can also obtain the same focusing by placing a uniform velocity on a spherical surface, which is the model we will use here. Thus, the form of the model is the same as the Rayleigh-Sommerfeld planar transducer model but we now have to integrate over a spherical surface.

## Slide 24
For x on the central axis
dS = r dr df/q0
q0 = 1 - z/R0
z
h
a
R0
x
re
r
Notes: On the axis of the transducer we can use the O’Neil model and, like the planar transducer case, obtain explicit results for the on-axis pressure.

## Slide 25
a = 6.35 mm
R0 = 76.2 mm
f= 10 MHz
c = 1480 m/s
Geometric focus
on-axis pressure versus z/R0:
True focus
0
0.5
1
1.5
2
2.5
3
3.5
4
0
2
4
6
8
10
12
z/R
|p|
rcv0
Notes: If we plot the on-axis pressure we see the pressure is enhanced near the geometrical focus where z/R =1 but the maximum pressure occurs at a slightly smaller distance called the true focus. As the frequency gets smaller the distance grows between the geometrical focus and the true focus. Again, we see rapid oscillations in the near field. However, unlike the planar transducer we can see one or more nulls beyond the maximum pressure location like the one seen here. In some cases, however, such nulls may not exist.

## Slide 26
function p = focused_on_axis(zR, A,c,F,R)
% on axis pressure of a spherically focused probe
% as a function of the normalized distance, zR = z/R
%A, radius of the transducer in mm. R , focal length in mm.
%c, the wave speed in m/sec, and F the frequency in MHz
al=1000*A*F/c;
ka=2*pi*al;
zN=(R/A)*(1/al)*(zR);
kz=ka*al*zN;
kR=2000*pi*F*R/c;
kh=kR-sqrt(kR^2-ka^2);
kre=sqrt((kz-kh).^2+ka^2);
p = (exp(i*kz) -exp(i*kre))./(1-kz./kR);
MAT> zR=linspace(.2,4,500);
MAT> p = focused_on_axis(zR,6.35,1480,10,76.2);
MAT> plot(zR,abs(p))
MAT> xlabel('z/R')
Notes: Here is the MATLAB code for the spherically focused transducer on-axis behavior.

## Slide 27
Paraxial Approximation
plane wave
diffraction coefficient
C1(a, z, R0 ,w)
q0 = 1 - z/R0
on-axis pressure:
Notes: In the paraxial approximation we can again represent the pressure as a plane wave term multiplied by a diffraction coefficient.

## Slide 28
|p|
rcv0
|p|
rcv0
exact
paraxial
on-axis pressure:
0
0.5
1
1.5
2
2.5
3
3.5
4
0
2
4
6
8
10
12
z/R
0
0.5
1
1.5
2
2.5
3
3.5
4
0
2
4
6
8
10
12
z/R
Notes: Comparing the exact and paraxial results we see again very good agreement. If the transducer is very tightly focused the paraxial approximation will not be accurate but most NDE transducers are not that tightly focused.

## Slide 29
function p = par_focused_on_axis(zR, A,c,F,R)
% on axis pressure of a spherically focused probe,paraxial approx.
% as a function of the normalized distance, zR = z/R
%A, radius of the transducer in mm. R , focal length in mm.
%c, the wave speed in m/sec, and F the frequency in MHz
al=1000*A*F/c;
ka=2*pi*al;
zN=(R/A)*(1/al)*(zR);
kz=ka*al*zN;
kR=2000*pi*F*R/c;
qo=1-kz./kR;
p = (1-exp(i*ka*(A/R)*qo./(2*zR)))./qo;
MAT> zR=linspace(.2,4,500);
MAT> p = par_focused_on_axis(zR,6.35,1480,10,76.2);
MAT> plot(zR, abs(p))
MAT> xlabel('z/R')
Notes: Here is the MATLAB code for the paraxial on-axis pressure

## Slide 30
Another way to model focusing (in the paraxial approximation)
O
suppose on a planar aperture we have a spherical wave propagating (generated by a lens, for example)
then on the aperture we have a phase given approximately
in the paraxial approximation by
Notes: Instead of using the O’Neil model we can model the effects of spherical focusing by considering an inward traveling spherical wave (as might be generated by a lens, for example) that is incident on a planar aperture. In the paraxial approximation we can examine the phase of this spherical wave.

## Slide 31
Thus, suppose we use a Rayleigh-Sommerfeld model for a planar transducer and place this phase (in the paraxial approximation) in the integral:
Using the paraxial approximation and evaluating this integral exactly for x on the transducer axis gives for a circular transducer of radius a:
Similarly, off-axis values will also represent those from a focused transducer
Notes: If we now insert that phase into the Rayleigh-Sommerfeld integral and perform the integrations in the paraxial approximation, we obtain an on-axis result which agrees with the O’Neil model in the paraxial approximation. Other points in the wave field will also agree. This method of generating focusing we will see later is very useful when we discuss a Gaussian beam model of the transducer wave field.

## Slide 32
a
R0
x
Wave field in the plane at the geometric
focus of a spherically focused transducer
p/pmax
-10
-8
-6
-4
-2
0
2
4
6
8
10
-0.2
0
0.2
0.4
0.6
0.8
1
1.2
Wf
l … wavelength
F = R0 / 2a … transducer
F number
kay/R0
q
Notes: Another case where we can evaluate the O’Neil model exactly is to obtain the wave field in a plane located at the geometric focus of the spherically focused transducer. We see that this field is controlled by a Bessel function behavior that is identical in form with that for the far field behavior of a circular piston transducer. An important measure of the wave field on this plane is the -6 dB beam width, Wf , where the peak amplitude has dropped to one half of its on-axis maximum value. We can show that this beam width is controlled by the wave length and the transducer F-number.

## Slide 33
On-axis response at normal incidence to an interface
(paraxial approximation)
z1
z2
fluid
solid
dp
transmission coefficient
(velocity/velocity)
same diffraction coefficient
expression as for a fluid
displacement
x
velocity
Notes: In the paraxial approximation we can also obtain an explicit expression for the on-axis velocity of a spherically focused P-wave transducer radiating at normal incidence into a solid through a plane interface. We simply multiply the result for a plane wave being transmitted through the interface by a diffraction coefficient which is the same as for the radiation into a fluid, but where the on-axis distance in the fluid case is replaced by an effective distance and the q0 focusing term also contains that effective distance.

## Slide 34
p0 … pressure
ST
n
x'
D
d1
d1
s
p
q’
x"
For bulk waves
D = |x' - x"|
Contact P-wave Transducer Model
solid
stress-free
surface
Notes: Now, consider a contact P-wave transducer sitting on the plane stress-free surface of an elastic solid. We cannot model this transducer as a piston source since the stiffness of the solid is likely the same order or larger than the stiffness of the transducer. However, since there is a thin fluid layer between the transducer and the solid, it makes sense to model the transducer instead as producing a uniform pressure over its active surface. We will see shortly that such a pressure will produce a complex set of waves, but an important set of those waves consist of radiating spherical P- and S- bulk waves that are contained in Rayleigh-Sommerfeld-like integrals, as shown above. Unlike the immersion transducer case, however, these integrals include directivity factors and polarization vectors.

## Slide 35
Directivity functions
Kp , Ks
Kp
Ks
0
10
20
30
40
50
60
70
80
90
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
1
angle, degrees
Notes: Here the directivity factors are plotted as a function of the angle from the normal to the surface.

## Slide 36
function [kp,ks] = directivity(ang, cp, cs)
% computes the directivity functions for a p-wave contact
%transducer. ang is angle in degrees, cp, cs are p- and s-wave %speeds
k = cp/cs;
angr = ang*pi/180;
x = sin(angr);
c =cos(angr);
g=(x.^2 -k^2/2).^2 + x.^2.*sqrt(1 - x.^2).*sqrt(k^2 - x.^2);
kp = c.*(k^2).*(k.^2/2 -x.^2)./(2.*g);
ks = (k*x <1).*c.*(k^3).*x.*sqrt(1 - k^2.*x.^2)./(2.*g);
MAT> x = linspace(0,90,200);
MAT> [kp,ks] = directivity(x, 5900, 3200);
MAT> plot(x, kp)
MAT> hold on
MAT> plot(x, ks)
MAT> xlabel('angle, degrees')
Notes: The MATLAB code for the directivities.

## Slide 37
For q' small Kp = 1, Ks = 0
Dp
R
Ep
Es
H
Dp … Direct P-wave
Ep … Edge P-wave
Es … Edge S-wave
H … Head wave
R … Rayleigh wave
Full set of waves :
integral
contains direct
and edge P-waves
Notes: Like the immersion case, a contact NDE transducer will operate at high frequencies where the transducer beam will be well-collimated and so the fields will be small when the angle from the transducer normal is not small. Thus, for small angles the S-wave directivity will be near zero and the P-wave directivity will be close to one, giving an expression for the displacement in the solid that is again in the form of a Rayleigh-Sommerfeld integral.
We have also shown above a more complete picture of all the waves generated by the contact transducer. We see a direct P-wave and edge P-waves seen previously in the immersion case (red lines). These waves are contained in the Rayleigh-Sommerfeld integral shown above. However, there are also edge S-waves generated and, when the edge P-waves graze along the free surface, additional “head” waves (also called “von Schmidt waves”) are generated that link the edge P- and S-waves. Finally, there are also Rayleigh waves that propagate primarily along and near the surface. Thus, the total wave field is rather complex. However, not too close to the transducer and near the transducer central axis, all the waves except the direct and edge P-waves will be small and the Rayleigh-Sommerfeld integral given above will model the wave response.

## Slide 38
Angle Beam Shear Wave Transducer Model
P
SV , SH
P
SV
P
SV
solid
solid
P
P
SV
“fluid”
solid
Can replace elastic
wedge by equivalent
"fluid" (neglect shear
waves)
(small for incident
P-wave beyond
critical angle)
Notes: If a contact transducer is placed on the surface of a wedge at an angle and the wedge is then placed on the surface of an elastic solid (usually with a thin fluid layer between the wedge and the solid) a complex set of transmitted P- and S-waves will be generated (the reflected waves are not shown since the wedge is usually designed to suppress their contributions). If the angle of the wedge is such that the direction of the P-wave in the wedge is above the first critical angle, then primarily an SV-wave will be generated in the solid, producing what is called an angle beam shear wave transducer (a small P-wave is present but it can normally be ignored). Since the waves present in this case are the same as those present for a fluid-solid interface, we can replace this configuration by an equivalent fluid-solid configuration and use an immersion transducer model, where we replace the transmission coefficient for a fluid-solid interface by the transmission coefficient for two solids in smooth (shear-stress -free) contact.

## Slide 39
Ultrasonic Beam Models
Numerically Intense Models
EFIT - K. Langenberg
Finite Elements – W. Lord
Boundary Elements – F. Rizzo
Edge Elements – L. Schmerr, T. Lerch
Surface Integral Models
Generalized Point Source – M. Spies
Rayleigh- Sommerfeld + High Freq. Asymptotics
- L. Schmerr, A. Lhemery, others
Line Integral Models
Boundary Diffraction Wave – L. Schmerr, T. Lerch
Notes: Our discussions in this section have centered around Rayleigh-Sommerfeld integral models of the sound beam generated by a transducer but there are many other transducer models available. There are numerically intense models representing the transducer surface (and in some cases the surrounding media) as a collection of very small elements. There are the surface integral models that superimpose spherical waves from point sources over the transducer face, and there are line integral models that superimpose a plane wave and boundary diffraction waves acting over the edge of the transducer.

## Slide 40
Ultrasonic Beam Models
Other Basis Function Models
Gauss-Hermite Models – B. Thompson, T. Gray, B. Newberry,
A. Minachi, F. Margetan
Multi- Gaussian Models
Minachi, M. Spies, L. Schmerr and M. Rudolph,
Cerveny (Seismology)
Notes: One can superimpose waves other than spherical waves to represent the transducer wave field such as Gauss-Hermite waves. However, one of the most effective models uses the paraxial approximation and the superposition of a small number of Gaussian beams. We will say more about a multi-Gaussian beam model later.

## Slide 41
Homework problems
8.1, 8.2 8.4, 8.5
Notes: Homework problems from Chapter 8.

## Slide 42
Ultrasonic Beam Models
A few references – mostly paraxial models
Lerch, T.P., Schmerr, L.W. and A. Sedov,” Ultrasonic beam models: an edge element
approach,” J. Acoust. Soc. Am., 104, 1256-1265, 1998.
Thompson, R. B. and E.F. Lopez,” The effects of focusing and refraction on Gaussian ultrasonic beams,” J. Nondestr. Eval., 4, 107-123, 1984.
Newberry, B.P. and R.B. Thompson,” A paraxial theory for the propagation of ultrasonic beams in anisotropic solids,” J. Acoust. Soc. Am., 85, 2290-2300, 1989.
Schmerr, L.W., Rudolph, M., and A. Sedov,” Modeling ultrasonic transducer wave fields
for general complex geometries and anisotropic materials,” Review of Progress in
Quantitative Nondestructive Evaluation, D. O. Thompson and D.E. Chimenti, Eds., Plenum Press, New York, 19A, 953-960, 2000.
Notes: Here are some references.

## Slide 43
Schmerr, L. W., Fundamentals of Ultrasonic Nondestructive Evaluation – A Modeling Approach, 2nd Ed. ,Springer, Switzerland, 2016.
Spies, M., and M. Kroning,” Ultrasonic inspection of inhomogeneous welds simulated by Gaussian beam superposition,” Review of Progress in Quantitative Nondestructive Evaluation, D. O. Thompson and D.E. Chimenti, Eds., Plenum Press, New York, 18A, 1107-1114, 1999.
Minachi, A., Margetan, F.J., and R.B. Thompson,” Reconstruction of a piston transducer beam using multi-Gaussian beams (MGB) and its applications,” Review of Progress in Quantitative Nondestructive Evaluation, D. O. Thompson and D.E. Chimenti, Eds., Plenum Press, New York, 17A, 907-914, 1989.
Gengembre,N. and A Lhemery," Calculation of wide band ultrasonic fields radiated by water-coupled transducers into heterogeneous media," Review of Progress in Quantitative Nondestructive Evaluation, D. O. Thompson and D.E. Chimenti, Eds., Plenum Press, New York, 18A, 1107-1131, 1999.
Ultrasonic Beam Models
Notes: More references. There are many, many more than listed here.