## Slide 1
Gaussian Beams and Transducer Modeling
Notes: This will be an overview of Gaussian beams and their use in transducer modeling.

## Slide 2
Learning Objectives
Characteristics of Gaussian Beams
Propagation Laws
Transmission/Reflection Laws
Multi-Gaussian Beam Models for Ultrasonic Transducers
MATLAB Examples
Notes: We will discuss some of the important properties of Gaussian beams and show how we can superimpose a small number of such beams to model a transducer wave field. We will also give a number of MATLAB examples of such a multi-Gaussian beam model.

## Slide 3
z
plane wave
spherical wave
Fundamental Waves as Building Blocks
R
Notes: We have already talked about two types of waves, plane waves and spherical waves, that can be used as fundamental building blocks for generating more complex wave fields.

## Slide 4
Gaussian beam
beam waist
beam width
confocal distance
Notes: A Gaussian beam is another fundamental building block. Here we will write out the Gaussian beam in a form that is rather complex looking but will be useful to discuss its properties. Later, we will express the Gaussian beam in more compact form. The Gaussian beam is a solution to the paraxial equation. We see that it has an amplitude term which is of the form of a Gaussian function and involves the beam width, which is a function of the distance z, the location of the beam waist where the beam width is w0 , and a distance parameter, zc , called the confocal distance.

## Slide 5
radius of curvature
beam waist
wave front radius
of curvature
Notes: There is also a term in the exponential which is a function of R(z), the radius of curvature of the wavefront. We see that for distances z greater than the beam waist location this radius is positive, representing an outward spreading wave. At very large z the radius is just the distance z, so it acts like a spherically spreading wave in the paraxial approximation. For distances z less than the beam waist location the radius is negative, representing an inwardly curving wave front. At the beam waist the radius of curvature is infinite so the wavefront is planar. Thus the Gaussian beam can represent many types of propagating waves.

## Slide 6
propagation term
amplitude term
Notes: We see that the Gaussian is propagating in the z-direction so it has the familiar propagation term we see for waves. There also is an amplitude term which is controlled by the distance z, the location of the beam waist, and the confocal parameter. For large z this is just the 1/z amplitude term we see for a spherical wave in the paraxial approximation.

## Slide 7
Gaussian beam
wave front curvature
Gaussian
profile
spherical wave (paraxial approximation)
can get from Gaussian beam by letting
Notes: If we compare the Gaussian beam with a spherical wave (in the paraxial approximation) we see there are many similarities. In fact, when the width at the beam waist and the beam waist location are both zero, the Gaussian beam coincides with the spherical wave expression.

## Slide 8
Paraxial Approximation
plane wave
write as
where
quasi-plane wave traveling
in the x3 –direction
Notes: We can get a more physical interpretation of the mathematical criterion for the paraxial approximation by looking at a plane wave that travels at a small angle from the z-axis. We can write this plane wave in terms of a quasi-plane wave traveling in the z-direction.

## Slide 9
Paraxial Approximation
if q <0.5 rad (about 30o)
Notes: If we look at the amplitude expression for this quasi-plane wave we see that is the angle is small (typically less than about 30 degrees from the z-axis) then the second derivative of this amplitude with respect to z is much less than the other derivatives shown, agreeing with the condition we stated earlier for the paraxial approximation to be valid. Thus, if a beam of sound is well collimated so that it does not spread too much, the paraxial approximation is valid.

## Slide 10
Paraxial Approximation
z
r
wave equation (cylindrical coordinates)
with axial symmetry
Let
and assume
then
paraxial wave equation
NOTE: r here is a radius, not the density
Notes: So far we have been looking at the wave equation in Cartesian or spherical coordinates. If we write the wave equation in cylindrical coordinates and examine a quasi-plane wave traveling in the z-direction, then the form of the paraxial wave equation is as shown.

## Slide 11
Paraxial Wave Equation
Solutions
plane wave
spherical wave
Gaussian beam
Notes: Here are the exact solutions to this paraxial wave equation for a plane wave, a spherical wave, and a Gaussian beam.

## Slide 12
Complex form of the Gaussian beam commonly used
Notes: We saw earlier that the Gaussian beam has a rather complex structure. However, we can write it in a much more compact form if we write the Gaussian in terms of a complex q function as shown.

## Slide 13
Gaussian beam amplitudes obey the plane wave relationship
density, not radius
Notes: Note that we can show that the Gaussian beam amplitudes as measured in terms of different quantities such as pressure (or stress) and velocity (or displacement) simply obey the plane wave relationships for those quantities we discussed earlier.

## Slide 14
z
Reflection and Transmission at a Spherical Interface of radius R0
Notes: One of the important properties of Gaussian beams is that we can propagate them through complex geometries and they always remain well-behaved. Consider, for example, the propagation of a Gaussian beam through a spherically curved interface at normal incidence. This is a very specific problem that we can use to show the process. We can write the incident, transmitted, and reflected Gaussians as shown.

## Slide 15
Amplitudes are related through plane wave reflection
and transmission coefficients
Phase terms are related by
transmitted beam
reflected beam
radius of interface
Notes: By matching the amplitudes and phases for pressure and velocity at the interface we can show that the amplitudes at the interface are related through plane wave reflection and transmission coefficients and the phase terms are also related.

## Slide 16
Transmission/reflection laws in terms of beam widths and
wave front curvatures
Notes: One finds that the beam widths match at the interface and we can also relate the wave front curvatures.

## Slide 17
(a)
(b)
Defocusing interface
Focusing interface
Notes: Suppose the beam waist of the incident wave is located at the interface. In this simple case one can easily see the effects of focusing or defocusing depending on the curvature of the interface. Even for a focusing interface the Gaussian beam remains well-behaved in the second medium, unlike a spherical wave which would lead to singularities.

## Slide 18
z
0
Notes: Consider a Gaussian beam that originates at some distance from the interface. We can write the incident and transmitted Gaussian beams as shown. We could also look at the reflected beam but in NDE problems we are often more concerned with the transmitted wave field.

## Slide 19
Gaussian beam transmitted through a planar interface
Gaussian beam in a single medium
Notes: Here is the expression for the transmitted Gaussian beam. We see that it has the same form as a Gaussian beam traveling in a single medium where we replace the z distance in the amplitude and Gaussian phase terms by an effective distance, a behavior we have seen before for other problems in the paraxial approximation.

## Slide 20
Gaussian beams in multiple media
Notes: In fact, we can easily write down the wave field of the Gaussian after propagation through multiple media. Multiple transmission coefficients are present but the form of the response remains very similar.

## Slide 21
Propagation Laws
Transmission Laws
Reflection Laws
Notes: We have seen that the q(z) function plays a key role in Gaussian beam theory. We can write down explicit propagation, transmission, and reflection laws in terms of this function.

## Slide 22
ABCD Matrix Forms of the Laws
Propagation Laws
Transmission Laws
Reflection Laws
Notes: In fact, we can write all these laws in a common form in terms of the elements of a 2x2 ABCD matrix.

## Slide 23
Gaussian beams in multiple media
transmission or reflection
coefficients
Notes: After transmission or reflection from multiple interfaces the Gaussian beam retains a simple form in terms of a single ABCD matrix that is obtained simply by multiplying all the individual ABCD matrices together.

## Slide 24
Gaussian beam in single medium
Gaussian beam after propagating through M+1 media
Notes: Here we see how the Gaussian beam retains its general form even in complex problems in terms of the ABCD matrices. This is for the very special case of normal incidence on the multiple interfaces present but a similar behavior is present in more general cases.

## Slide 25
Multi-Gaussian Beam Model
circular piston transducer radiating into a fluid
add ten Gaussians
a
Notes: Gaussian beams can be used to develop a very efficient beam model for a circular piston transducer. Wen and Breazeale showed that one can simply superimpose as few as 10 different Gaussians on the face of the transducer to produce the same wave field that is generated by a uniform velocity (piston) transducer. These Gaussians will then produce ten propagating Gaussian beams that we can be propagated in the manner we have just discussed. This is a multi-Gaussian beam model.

## Slide 26
add ten Gaussians
Notes: Here, for example, is a multi-Gaussian beam model for a single medium. It is expressed in terms of ten known complex-valued coefficients An , Bn .

## Slide 27
function [a, b] = gauss_c
% gauss_c returns the coefficients developed by Wen and Breazeale to model a
% piston transducer
a = zeros(10,1);
b = zeros(10,1);
a(1) = 11.428 + 0.95175*i;
a(2) = 0.06002 - 0.08013*i;
a(3) = -4.2743 - 8.5562*i;
a(4) = 1.6576 +2.7015*i;
a(5) = -5.0418 + 3.2488*i;
a(6) = 1.1227 - 0.68854*i;
a(7) = -1.0106 - 0.26955*i;
a(8) = -2.5974 + 3.2202*i;
a(9) = -0.14840 -0.31193*i;
a(10) = -0.20850 - 0.23851*i;
b(1) = 4.0697 + 0.22726*i;
b(2) = 1.1531 - 20.933*i;
b(3) = 4.4608 + 5.1268*i;
b(4) = 4.3521 +14.997*i;
b(5) = 4.5443 + 10.003*i;
b(6) = 3.8478 + 20.078*i;
b(7) = 2.5280 -10.310*i;
b(8) = 3.3197 - 4.8008*i;
b(9) = 1.9002 - 15.820*i;
b(10) = 2.6340 + 25.009*i;
Notes: Here are the ten coefficients obtained by Wen and Breazeale.

## Slide 28
Multi-Gaussian beam model of a piston
transducer in multiple media
Notes: These ten Gaussians can then be transmitted or reflected multiple times to obtain the Gaussian beam in the final medium.

## Slide 29
multi-Gaussian beam model for a
spherically focused circular transducer
add ten Gaussians
F
a
Notes: A multi-Gaussian bean can also easily model a spherically focused transducer by simply including an additional phase term at the transducer face, as previously discussed. This term can be easily included by simply changing the Bn coefficients in the multi-Gaussian model.

## Slide 30
MATLAB multi- Gaussian Beam Model
z
a
F
x
% MGB_script
% This script calculates the normalized
% pressure, p/p0, due to a planar piston transducer radiating at normal
% incidence through a spherically curved interface.
% This is a multi-Gaussian beam model that uses the 10 coefficients
% of Wen and Breazeale to calculate the wave field.
clear % clear the workspace so that any previous parameter choices % are eliminated
The time delay factor is not included in this model
Notes: We will illustrate a multi-Gaussian beam model by considering the radiation of a planar or spherically focused piston transducer through a spherically curved interface at normal incidence, as shown above. A MATLAB script, MGB_script, will be developed explicitly for this problem. The script first clears the workspace so that any parameters remaining from a previous calculation are removed.

## Slide 31
z
a
F
x
r
omit
Notes: Here is the explicit expression we will use and the definition of all the underlying parameters. We do not use ABCD matrices here since it is a very simple case. We will not include the propagation phase term here since that term simply provides a time delay term for the arriving waves but does not affect their spatial distribution. The q1 function describes the behavior of the Gaussian beam in the first medium and the q2 function describes its behavior in the second medium. T12 is the plane wave transmission based on pressure ratios. Shown is a single term in a ten-term multi-Gaussian beam model.

## Slide 32
MATLAB multi- Gaussian Beam Model
% get input parameters
f = 5; %frequency (MHz)
a = 6.35; % transducer radius (mm)
Fl = inf; % transducer focal length (mm)
z1 = 0; % path length in medium 1 (mm)
z2 = linspace(6, 125, 200); % path length in medium 2 (mm)
r =0.0; % distance from ray axis (mm)
R0 = inf; % interface radius of curvature (mm)
d1 = 1.0; % density, medium 1 (gm/cm^3)
d2 =1.0; % density, medium 2 (gm/cm^3)
c1 = 1480.; % wave speed, medium 1 (m/sec)
c2 = 1480.; % wave speed, medium 2 (m/sec)
These parameters are for a ½ inch diameter, 5 MHz planar
piston transducer radiating into water (no interface). The on-axis
pressure values from 6 to 125 mm are being sought.
Notes: Here are the input parameters in the script. The default case is where we are radiating into a single medium and calculating the on-axis normalized pressure from 6 mm to 125 mm on the transducer axis for a planar piston transducer.

## Slide 33
MATLAB multi- Gaussian Beam Model
% get Wen and Breazeale coefficients (10)
[A, B] = gauss_c;
% transmission coefficient (based on pressure ratio)
T = (2*c2*d2)/(c1*d1+c2*d2);
h = 1/R0; % interface curvature
zr = eps*(f == 0) + 1000*pi*(a^2)*f./c1; % "Rayleigh" distance, ka^2/2
k1 = 2*pi*1000*f./c1; % wave number in medium 1
Notes: We also need the Wen and Breazeale coefficients and we define curvature of the interface in terms of the radius. Two parameters, the Rayleigh distance and the wave number associated with the first medium are also defined.

## Slide 34
MATLAB multi- Gaussian Beam Model
%initialize pressure to zero
p = 0;
%multi-Gaussian beam model
for j = 1:10 % form up multi-Gaussian beam model with
% 10 Wen and Breazeale coefficients
b =B(j) + i*zr./Fl; % modify coefficients for focused probe
q = z1 - i*zr./b;
K = q.*(1 -(c1/c2));
M = (1 +K.*h);
ZR = q./M;
m = 1./(ZR +(c2/c1).*z2);
t1 = A(j)./(1 + (i.*b./zr).*z1);
t2 = t1.*T.*ZR.*m;
p = p + t2.*exp(i.*(k1./2).*m.*(r.^2));
end
Notes: We then simply add up ten Gaussian beams of the form shown previously, changing the Wen and Breazeale coefficients for the focused case ( Fl = inf for a planar interface) to compute the normalized pressure.

## Slide 35
0
20
40
60
80
100
120
140
0
0.5
1
1.5
2
2.5
z-axis
|p|/|po|
%plot magnitude of on-axis pressure
plot(z2, abs(p))
xlabel('z-axis')
ylabel('|p|/|po|')
>> MGB_script
Notes: After executing the MGB_script, we plot the on axis pressure, showing the near field behavior of the planar piston transducer.

## Slide 36
Cross-axis plot at z = 130 mm (near last maximum)
% get input parameters
f = 5; %frequency (MHz)
a = 6.35; % transducer radius (mm)
Fl = inf; % transducer focal length (mm)
z1 = 0; % path length in medium 1(mm)
z2 = 130; % path length in medium 2 (mm)
r =linspace(-10, 10, 200); % distance from ray axis (mm)
R0 = inf; % interface radius of curvature (mm)
d1 = 1.0; % density, medium 1 (gm/cm^3)
d2 =1.0; % density, medium 2 (gm/cm^3)
c1 = 1480.; % wave speed, medium 1 (m/sec)
c2 = 1480.; % wave speed, medium 2 (m/sec)
Notes: Now, let us change the input parameters in the script (changes in red) and plot the pressure versus radius at a distance near the last on-axis maximum. Save the script with these changes and execute.

## Slide 37
%plot magnitude of on-axis pressure
plot(r, abs(p))
xlabel('r-axis')
ylabel('|p|/|po|')
>> MGB_script
-10
-8
-6
-4
-2
0
2
4
6
8
10
0
0.2
0.4
0.6
0.8
1
1.2
1.4
1.6
1.8
2
r-axis
|p|/|po|
Notes: Here is a plot of the off-axis pressure versus the radius near that last maximum in the near field, showing a main lobe and some side lobes for the beam

## Slide 38
Cross-axis plot at z = 65 mm (near last on-axis null)
% get input parameters
f = 5; %frequency (MHz)
a = 6.35; % transducer radius (mm)
Fl = inf; % transducer focal length (mm)
z1 = 0; % path length in medium 1 (mm)
z2 = 65; % path length in medium 2 (mm)
r =linspace(-10, 10, 200); % distance from ray axis (mm)
R0 = inf; % interface radius of curvature (mm)
d1 = 1.0; % density, medium 1 (gm/cm^3)
d2 =1.0; % density, medium 2 (gm/cm^3)
c1 = 1480.; % wave speed, medium 1 (m/sec)
c2 = 1480.; % wave speed, medium 2 (m/sec)
Notes: Now, let us look instead at the cross axis behavior at a distance close to the last on-axis null in the near field.

## Slide 39
>> MGB_script
-10
-8
-6
-4
-2
0
2
4
6
8
10
0
0.2
0.4
0.6
0.8
1
1.2
1.4
r-axis
|p|/|po|
%plot magnitude of on-axis pressure
plot(r, abs(p))
xlabel('r-axis')
ylabel('|p|/|po|')
Notes: We see pressure is small near the null on the axis but has large values off axis.

## Slide 40
Now, generate an image of the entire beam
% get input parameters
f = 5; %frequency (MHz)
a = 6.35; % transducer radius (mm)
Fl = inf; % transducer focal length (mm)
z1 = 0; % path length in medium 1 (mm)
z2t = linspace(0,200,500);
rt =linspace(-20, 20, 200);
[z2, r]=meshgrid(z2t, rt);
R0 = inf; % interface radius of curvature (mm)
d1 = 1.0; % density, medium 1 (gm/cm^3)
d2 =1.0; % density, medium 2 (gm/cm^3)
c1 = 1480.; % wave speed, medium 1 (m/sec)
c2 = 1480.; % wave speed, medium 2 (m/sec)
Notes: To see a cross section of the entire beam we need to change the script to generate a grid of points in the two-dimensional (r, z) plane.

## Slide 41
%plot magnitude of the pressure
image(z2t, rt, abs(p)*50)
xlabel('z-axis')
ylabel('r-axis')
>> MGB_script
Note: unequal scales
Notes: Here is an 2-D image of the transducer wave field showing its complex behavior (at a given frequency) in the near field. The magnitude of the pressure has been multiplied by a factor here so the colors in the image give a good visual of the wave field.

## Slide 42
We can also examine a 10 MHz, 76.2 mm focal length
focused transducer
% get input parameters
f = 10; %frequency (MHz)
a = 6.35; % transducer radius (mm)
Fl = 76.2; % transducer focal length (mm)
z1 = 0; % path length in medium 1(mm)
z2 = linspace(0,200,500); % path length in medium 2 (mm)
r=0; % distance from ray axis (mm)
R0 = inf; % interface radius of curvature (mm)
d1 = 1.0; % density, medium 1 (gm/cm^3)
d2 =1.0; % density, medium 2 (gm/cm^3)
c1 = 1480.; % wave speed, medium 1 (m/sec)
c2 = 1480.; % wave speed, medium 2 (m/sec)
Notes: Now let us consider a 10 MHz spherically focused transducer radiating into water and examine the on-axis behavior.

## Slide 43
%plot magnitude of on-axis pressure
plot(z2, abs(p))
xlabel('z-axis')
ylabel('|p/po|')
>> MGB_script
0
20
40
60
80
100
120
140
160
180
200
0
2
4
6
8
10
12
z-axis
|p/po|
Notes: Here is the on-axis plot, showing the large pressure near the focus, the near-field behavior, and the existence of the null (shown previously) at a distance greater than the focal length.

## Slide 44
Now, plot an image of this focused transducer wave field
% get input parameters
f = 10; %frequency (MHz)
a = 6.35; % transducer radius (mm)
Fl = 76.2; % transducer focal length (mm)
z1 = 0; % path length in medium 1 (mm)
z2t = linspace(0,300,500);
rt=linspace(-20,20,200);
[z2, r]=meshgrid(z2t, rt);
R0 = inf; % interface radius of curvature (mm)
d1 = 1.0; % density, medium 1 (gm/cm^3)
d2 =1.0; % density, medium 2 (gm/cm^3)
c1 = 1480.; % wave speed, medium 1 (m/sec)
c2 = 1480.; % wave speed, medium 2 (m/sec)
Notes: Here we change the script to show a 2-D cross-sectional image.

## Slide 45
%plot magnitude of the pressure
image(z2t, rt, abs(p)*25)
xlabel('z-axis')
ylabel('r-axis')
>> MGB_script
Note: unequal scales
Notes: Comparing with the previous planar case we clearly see the effects of focusing. We can consider many other cases but we will stop here.

## Slide 46
Homework problems
F.2, F.3
Notes: Homework problems from Appendix F.