## Slide 1
Statistical Foundations of Pattern Recognition
Notes: We will give a very brief overview here of how we can use statistical methods to evaluate the meaning of ultrasonic NDE flaw signals.

## Slide 2
Learning Objectives
Bayes Theorem
Decision-making
Confidence factors
Discriminants
The connection to neural nets
Notes: An ultrasonic NDE flaw measurement is an indirect measurement in that we normally have a measured output such as a voltage versus time trace received from the flaw which we must interpret to determine the flaw characteristics such as size, type (e.g. crack or inclusion) or material properties, etc. We can view many of these problems as pattern recognition problems. Statistical methods based on probabilities have long been used in this task so we will examine a statistical approach to the decision-making process in pattern recognition, based on Bayes theorem, which we will define shortly. We will go through some simple examples and introduce uncertainties in the decision-making process with the use of confidence factors.
We will see how the underlying probabilities can be replaced by quantities called discriminants and how we can learn such discriminants directly from the underlying data. We will connect this learning process to a simple form of a neural network. Neural nets are powerful pattern recognition tools that we will discuss more extensively in a separate presentation.

## Slide 3
NDE measurement system
feature (pattern)
extraction
observed patterns
possible classes
?
Problem: How do we decide
which class xk belongs to
Notes: In an ultrasonic NDE flaw measurement system we can obtain some “raw” (i.e. unprocessed) flaw signals and then use those signals to extract some specific features from the signals in the form of observed patterns. The problem we want to consider here is: given an observed pattern of features and a set of possible classes of flaws from which it could come, how do we decide which class to choose? We will give a simple example shortly that will tie this general pattern recognition task more closely to an ultrasonic measurement but first we need to define some of the probabilities that we will be talking about when we use Bayes theorem as part of the decision-making process.

## Slide 4
Bayesian (probabilistic) approach
Let
= apriori probability that a pattern belongs to class ci, regardless of the identity of the pattern
= apriori probability that a pattern is xk , regardless of its class membership
= conditional probability that the pattern is xk , given that it belongs to class ci
= conditional probability that the pattern's class membership is ci , given that the pattern is xk
= the joint probability that the pattern is xk and the class membership is ci
Notes: A Bayes approach is based on probabilities, but there are number of different types of probabilities we must consider. There are two a priori probabilities. There is the a priori probability that the pattern we see comes from a specific class and the a priori probability that we will see a given pattern. There are also two conditional probabilities. There is the probability that a given pattern is present when a measurement is done on a particular class and the probability that a particular class is present given that we see a given pattern. Finally, there is a joint probability that both a given pattern and given class are both present.
In the next slide we will put some more specific flesh on the meaning of these probabilities.

## Slide 5
Example: consider the case where there is one pattern value that is observed or not, and two classes (e.g. signal or noise)
x, c1 *
~x, c1
x, c1 *
~x, c2
x, c2 #
x, c1 *
x, c2 #
~x, c1
~x, c1
x, c1 *
(~x means x not observed)
Then
(see * s)
(see # s)
Notes: Consider the flaw detection problem of distinguishing between whether we are seeing a flaw signal or are simply seeing “noise.” Here there are obviously two classes : c1: flaw signal and c2: noise (no flaw). Suppose we use the amplitude of the flaw voltage signal to make that decision and set a voltage threshold value above which we say we have observed a flaw, a pattern feature we will label as x, and below which we say we have not observed a flaw, a pattern feature we will label as ~x. Now, let us take ten measurements on samples containing either flaws or no flaws and suppose the ten results are as shown above. Then from examining those cases we can determine a priori probabilities. conditional probabilities, and joint probabilities, as shown. Of course these are very few samples so we should not take probability values based on such a small amount of data too seriously. They are simply meant to illustrate the meaning of the various probabilities we defined.

## Slide 6
Bayes Theorem
or, equivalently, in an "updating form"
"old"
probability of ci
"new" probability of ci , having seen xk
Notes: Bayes theorem connects these probabilities since it says we can write the joint probability in terms of either sets of conditional probabilities and a priori probabilities, as shown. We can write this theorem in a form where given a set of a priori probabilities and a set of measurements, we can give an “updated” probability (from the original a priori probability that of a given class) that a given class is present, based on the conditional probability that we have a set of features from that class .

## Slide 7
Since
we can calculate if we know the probabilities
Bayes Theorem
and
Notes: In Bayes theorem it appears we need to have three probabilities to do an “updating” but in reality we only need the a priori probabilities of the classes present and conditional probabilities that a measured pattern feature comes from a particular class.

## Slide 8
Now, consider our previous example
or, in the "updating" form
Notes: Here is our previous example of ten measurements, where we see that the various probabilities are indeed related through Bayes Theorem. Of course, this is an artificial “static” example where we have simply used Bayes theorem to relate the various probabilities from a set of known examples. The real power of Bayes theorem comes when we use the updating form of that theorem in a “dynamic” setting to provide an improved decision of what we are seeing based on new data as it comes in. We will give a specific example of this next.

## Slide 9
As a simple example, consider trying to classify a flaw as a crack or a volumetric flaw based on the these two features:
x1 : a positive leading edge pulse, PP
x2 : flash points, FP
Notes: Cracks are typically more dangerous flaws than are volumetric flaws such as inclusions. Thus, suppose we consider trying to classify a flaw as a crack or non-crack (volumetric flaw). From our discussions of flaw scattering we know an isolated crack will produce a pair of negative and positive flashpoint signals in the time domain, as shown. A volumetric flaw, on the other hand, will often produce a large leading edge response, which may be positive or negative, depending on the acoustic impedance of the flaw relative to the surrounding material. A positive leading edge response will likely be easier to distinguish from a set of flashpoints, so let us choose a positive leading edge response and flashpoints as the two features we will use to classify an unknown flaw signal. Of course we will have to do some processing of the raw time domain signals to determine if either feature is present, but let us assume that processing is done and a criterion is chosen so that we can determine the existence of these features from the signals.

## Slide 10
Assume:
P( crack ) =0.5
P( volumetric ) = 0.5
P( PP | crack) = 0.1 (cracks have leading edge signal that is always negative, so unless the leading edge signal is mistakenly identified, this case is unlikely)
P( PP | volumetric ) = 0.5 (low impedance (relative to host) volumetric flaws have negative leading edge pulses and high impedance volumetric flaws have positive leading edge pulses, so assume both types of volumetric flaws equally likely)
P( FP | crack )= 0.8 ( flashpoints is a features strongly characteristic of cracks, so make this probability high)
P( FP | volumetric ) =0.05 (alternatively, make this a very low probability)
Notes: Now, we need to set up the probabilities present in Bayes Theorem. These could come with previous experience from tests done on samples with know flaws or they could come from educated estimates.

## Slide 11
(1) Now, suppose a piece of data comes in and there is firm evidence that flashpoints (FP) exists in the measured response. Then what is the probability that the flaw is a crack?
Thus, we also have
Notes: Now, let us use Bayes Theorem as we do testing on a sample with a flaw that is unknown. Here is an example where our processing of the signals gives a firm indication of flashpoints. Flashpoints are strong indicators of cracks so we see our updated estimate of the probability that the flaw is a crack is very high, certainly much higher than the 50/50 probability we started out with.

## Slide 12
(2) Now, suppose another piece of data comes in with the firm evidence of a positive leading edge pulse (PP). What is the new probability that the flaw is a crack?
and, hence
Note how the previous was now taken as the new, apriori
in this Bayesian updating
Notes: Now we use another data sample such as a measurement of the flaw from a different angle, where there is firm evidence of a positive leading edge signal. We see how the probability that the flaw is a crack has been reduced by this new data.

## Slide 13
(3) Finally, suppose another data set comes in with firm evidence that the flashpoints (FP) do not exist (written as ~FP). What is the probability now
that the flaw is a crack?
and now
Note:
Notes: We could also have a data sample where there is firm evidence that flashpoints do not exist. We can again use Bayes theorem in this case. Of course the new estimate of the probability that the flaw is a crack, given that we are certain that flashpoints are not present in this case, has been significantly reduced.

## Slide 14
In all three cases we must make some decision on whether the flaw is a crack or not. One possible choice is to simply look at the probabilities and decide xk belongs to class c = cj if and only if
for all
Since in our present example we only have two classes, we only have the
two conditional probabilities
and since , our decision rule is just
or
Notes: Bayes theorem gives us updated probabilities but we still need to use those probabilities to make a decision on whether the flaw is a crack or not. We could simply choose the conditional probability output from Bayes theorem which is the largest. Since there are only two classes in this case, this means we would make a decision when the output conditional probability is bigger than 0.5.

## Slide 15
Using this simple probability decision rule, in the previous three cases we would find
(1)
(2)
(3)
crack
crack
volumetric
There is no reason, however, that we need to make a decision on the conditional probabilities by themselves.
We could synthesize a decision functions from such conditional
probabilities and use the instead. This is the idea behind what is
called Bayes Decision Rule:
decision
Notes: Based on this type of decision process, here are the classification decisions we would make after our three tests. However, there is no reason to only use the probabilities themselves. We could instead define a decision function which is based on those probabilities, leading to what is called Bayes decision rule.

## Slide 16
Bayes Decision Rule
Decide xk belongs to class c = cj if and only if
for all
where
is the decision function for class ci
Notes: If we have generated such a decision function here is Bayes decision rule.

## Slide 17
Example: Suppose that not all decision errors are equally important. We could weight these decisions by defining the loss, lij that is sustained when we decide class membership is ci when it is in reality class cj . Then in terms of these losses we could also define the risk that xk belongs to to class ci as
For our two class problem we would have
The decision rule in this case would be to decide xk belongs to class c1 if and only if
or, equivalently
Notes: Here is an example of setting up such a decision function by including estimates of the losses sustained when we do a misclassification to construct a risk function that we will use in our decision-making instead.

## Slide 18
In the special case where there is no loss when we guess correctly, then l11 = l22 = 0. If, also it is equally costly to guess either c1 or c2 then l12 = l21 and the decision rule becomes
or
which is the simple decision rule based on conditional probabilities we discussed previously
Notes: Note that this risk function approach also includes the special case of just using conditional probabilities as a special case.

## Slide 19
Now, consider our previous example again and let c1 = crack,
c2 = volumetric flaw and suppose we choose the following loss factors:
(a gain. If we guess cracks, which are dangerous, correctly we should reward this decision)
(if we guess that the flaw is a crack and it is really volumetric, then there is a cost (loss) since we may do unnecessary repairs or removal from service)
(if we guess the flaw is volumetric and it is really a crack, there may be a significant loss because of a loss of safety due to misclassification)
(if we guess it is volumetric and it is , there might be no loss or gain)
Notes: To construct the risk function we need to choose the loss factors. These factors may come, for example, from historical data or from safety concerns. Here is a set of choices for the loss factors.

## Slide 20
In this case we find the decision rule is – decide that a crack is present if
or
For our example then we have
(1)
decision
c1 (crack)
(2)
c1 (crack)
(3)
c1 (crack)
Notes: If we use this risk function in our decision-making process with the previous three test examples, here are the decisions. Note how the losses have significantly affected our final decision.

## Slide 21
Bayes Theorem (Odds)
We can also write Bayes Theorem in terms of odds rather than probabilities by noting that for any probability P (condition, joint, etc.) we have the corresponding odds, O, given by
Example:
Using this definition of odds, Bayes Theorem becomes
where
is called the likelihood ratio
( or )
Notes: Instead of using probabilities we could also write Bayes theorem in terms of odds, since we are accustomed to dealing with odds in a number of venues. In this form we see that the odds are simply updated by the likelihood ratio, LR, which is defined here

## Slide 22
Going back to our example with x1 =PP, x2 =FP
Then for our three cases:
Notes: Here is our previous example of a two class problem with the two features of flash points and positive leading edge pulse, where we show all the odds corresponding to our original probabilities.

## Slide 23
(1)
and
(2)
and
(3)
and
Notes: Here are the results of our three experiments in terms of the resulting conditional odds.

## Slide 24
As we see from this result we can update the probabilities according to Bayes Theorem by
if the feature pattern xk is observed and by
if the feature pattern xk is not observed. We can combine these two cases as
where
and
if xk is observed
if xk is not observed
Notes: Here we show that we can use the same form of Bayes theorem if a feature is observed or not observed by combining the two cases into the same form but with different likelihood ratios.

## Slide 25
Criticisms of this Probabilistic Approach
It does not include uncertainty in the evidence of the existence (or not) of the feature patterns
2. It is difficult to assign the apriori probabilities
To solve the first problem we will show how to introduce uncertainty with confidence factors
To solve the second problems, we will discuss the alternative use of discriminants
Notes: Notice that there are two problems with this simple use of Bayes theorem. First, we always assumed there was firm evidence (by which we meant certainty) that a feature was present or not. Second, we had to assign initially the a priori probabilities, but gave no way to actually do that assignment in a given problem. Thus, we will now try to address those problems.

## Slide 26
Confidence Factors
Consider Bayes Theorem in the odds form
In updating the odds, the likelihood ratio is based on being able to have firm evidence of the existence of the pattern xk or not
We can introduce uncertainty into this updating by letting a user (or a program) give a response R in the range [-1,1], where
R = 1 corresponds to complete certainty xk is present
R = 0 corresponds to complete uncertainty that xk is or is not present
R = -1 corresponds to complete certainty that xk is not present
Notes: We can introduce uncertainty in the updating of odds with Bayes theorem by intruding a confidence factor, R, which varies from -1 to 1 as indicated here.

## Slide 27
Then in updating the odds, we can replace the likelihood ratio, LR, by a function of LR and R that incorporates this uncertainty
There are, however, some properties that this function f should satisfy.
They are:
if R = 1
(if we are certain in the evidence of xk , we should reduce to ordinary Bayes)
2. If R = -1
(if we are certain xk does not exist, again reduce to ordinary Bayes)
3. If LR = 0 , f = 0
(if the likelihood is zero, regardless of the uncertainty, R, the updated odds should
be zero)
Notes: We then can replace the likelihood ratio in Bayes theorem with a modified likelihood function that includes this confidence factor. Here are some properties such a function should have.

## Slide 28
A popular choice that appears in the literature is to choose
where, if R [0,1]
and, where, if R [-1,0]
If we plot this function, we see the effects of R
-1
1
R
1.0
Notes: Here is a piece-wise linear function one often sees in the literature.

## Slide 29
Although this is a simple function to use, there is a problem with it which we can see if we plot f versus LR for different |R|. ( Note that LR [0, ) )
LR
|R| =1
1.0
1.0
|R| =0
1-|R|
|R| increasing
|R| increasing
At LR = 0 the function f does not go to zero as we said it should (see property 3 discussed above). To remedy that problem, we need to choose a nonlinear function.
Notes: However, this choice does not satisfy the third property we gave earlier. Thus, we need to choose a different, nonlinear function.

## Slide 30
LR
|R| =1
1.0
1.0
|R| =0
|R| increasing
|R| increasing
One choice that satisfies all three properties f should have is
Notes: Here is one choice of such a nonlinear function which does have all the three properties listed earlier.

## Slide 31
This gives a dependency on R that is nonlinear
R
0
1
-1
1.0
Notes: This function is also nonlinear in R

## Slide 32
With this choice of f, we would have
However, if one wants to work in terms of probabilities, not odds, we have
with
and
Notes: With this choice of the function then we can write Bayes theorem either in terms of odds or probabilities in forms that allow us to adjust the updating in a manner which allows us to incorporate uncertainty that the features are present in the decision-making process.

## Slide 33
Bayes theorem, even in this modified form to take into account uncertainty in the evidence, still requires us to have apriori probability estimates and those may be difficult to come by. How do we get around this?
Consider our two class problem where we have classes (c1, c2 ) and where xk =x is a single feature (pattern). According to Bayes decision rule we could decide on c1 (or c2 ) if g1(x) > g2(x) (or g2(x) > g1(x) ). For example, suppose both g1 and g2 were unimodal, smooth distributions. Then we might have:
decide c1
decide c2
x
Then we see the decision rule is really just
Notes: Now, let us turn our attention to the problem of having to give the a priori probabilities. In the two class problem we have been examining where we use Bayes decision rule, consider if there was only one feature, x, being used. Then the decision functions might look like two smooth functions having peaks at different values of x so that we could distinguish between the two classes. However, if instead of using the functions themselves to make a decision, we see we could instead just use a threshold value for x (where the two functions are equal) to make the decision.

## Slide 34
Thus, if we had a way of finding , which serves as a discriminant, we could make our decisions and not have to even consider the underlying probabilities!
However, we have not really eliminated the probabilities entirely since they ultimately determine the errors made in the decision making process.
Note that in the more general multi-modal decision function case, several discriminants may be needed:
Notes: If we had a way to determine the threshold in this single feature case, we could then base our decisions directly on that threshold value so that value serves as a discriminant. In cases where the behavior of the underlying decision functions were more complex, we might need several discriminants as shown in this example.

## Slide 35
If we take the gi(x) to be just the probability distributions
then recall that Bayes decision rule says that xk belongs to class c = ci if and only if
for all
or, equivalently
which says that
so that also
If x is a continuous variable, then we can associate probability distributions with quantities such as p( ci, x ) and p( x | ci) and so we expect that the discriminants are dependent on the nature of these distributions. We will now examine closer that relationship.
Notes: Here is Bayes decision rule for one feature x and where we have multiple possible classes, written in terms of probabilities. If x is a continuous variable than we could replace these discrete probabilities with probability distributions (as a function of x) and try to determine the discriminants from these distributions.

## Slide 36
Probability Distributions and Discriminants
First, consider the 1-D case where x = x and where we assume the distributions are Gaussians, i.e.
where
mean value of x for class ci
standard deviation for class ci
If we assume
then Bayes decision rule
says that x belongs to class ci if and only if
Notes: Now, consider the case where there is one feature, x, which has continuous values, and assume the joint probability distributions for the various cases are Gaussians with different mean values and standard deviations. Note that Gaussians are smooth, peaked functions of the type we considered previously. Then if, for example, we assume the a priori probabilities are the same for all the classes then we can write the Bayes decision rule solely in terms of the properties of these Gaussians.

## Slide 37
or, equivalently,
x belongs to class ci if and only if
This is just the basis for the nearest cluster center classification method
for all
Notes: However, it is only the mean values of the Gaussians that determine the class, so those mean values act as discriminants and we could write our decision process in a form which is called the nearest center cluster classification method. Thus, here is a simple example where we can replace the underlying probabilities with dicriminants.

## Slide 38
Now, consider the more general case of N-dimensional features but keep the assumption of Gaussian distributions. Then
where
… N-component mean vector for class ci
… N x N covariance matrix
Notes: Let us generalize this problem by considering the more realistic case of multiple features and multiple classes. However, we will continue to use Gaussians which now must be written in terms of vectors and matrices. Do not be put off by these more complex forms since we will see much of this complexity can reduce eventually to a more understandable result.

## Slide 39
Bayes decision theory says that x belongs to class ci if and only if
Now, suppose we are on the boundary between ci and cj and also suppose that
where I is the unit matrix. Then
Taking the ln of this equation then we have
Notes: Here is Bayes decision theory in terms of these Gaussians. We will assume all the standard deviation matrices are identical in terms of a scalar standard deviation value and look at the case when we are on the decision boundaries between classes, since we know that is where a discriminant can exist between those classes. Taking the natural log of the expression seen in Bayes decision theory then gives the results seen on the next slide.

## Slide 40
which can be expanded out to give
However, these are just the equations of the hyperplanes
with
Notes: The form of this result can be expanded out and written in matrix-vector form which shows that the boundaries defined between the classes are hyperplanes that are characterized by w and b matrices.

## Slide 41
The wij and the bij here determine the hyperplanes separating the classes and hence are discriminants. If we can find a way to determine these discriminants directly, we need not deal with the underlying probabilities that define them. We will now examine ways in which we can find such hyperplanes (or hypersurfaces in a more general context).
Notes: The w and b matrices are our discriminants. Notice that the b matrices depend on the a priori probabilities but if we can find these discriminants directly then we do not need to know those a priori probabilities. Thus, we now need to determine a way to obtain such discriminants. we will give now a simple example of how to do that.

## Slide 42
Learning Discriminants with Neural Networks
Suppose that we have a two class problem and a linear discriminant is able to distinguish between observed patterns, x, of either class. Such a problem is said to be linearly separable.
Geometrically, we have the situation where we can place a discriminant hyperplane
between patterns, x, of either class. For example, for x = (x1 , x2 )
class c1
class c2
= pattern observed from class c2
= pattern observed from class c1
Notes: In the following slides we will examine a two class problem where we use two features simultaneously to determine the class of a flaw. If we can define a line in this two dimensional feature space which acts as a discriminant between the two classes then we say that this is a linearly separable classification problem. The discriminating line here can be defined by a 2-D vector w = [ w1, w2 ] which is normal to the line and a scalar b which represents the perpendicular distance from the origin to the line.
We will show that we can define a learning procedure that can directly determine the separating line discriminant and show how this procedure is similar to a neural network model where we use only a single model of a “neuron”. In a later presentation , we will generalize these ideas to more detailed neural networks consisting of many “neurons”

## Slide 43
Learning to distinguish between these two classes then consists of finding the values of w, b that will separate the observed patterns.
Note that we can augment the vector
and the weight vector
by redefining them as
Then the equation of the hyperplane in terms of these augmented vectors becomes
Notes: To connect this linearly separable problem more closely to neural networks, let us incorporate the b constant into the weight vector, w, and similarly augment the vector x as shown. Then the hyperplane takes the simple form shown.

## Slide 44
This equation can be related to neural network ideas since we can view the process of making a decision c1 or c2 as similar to the firing (or not firing) of a neuron based on the activity level of the inputs:
class c1
class c2
Now, the question is, how do we determine the unknown "weights", w, b ?
Notes: In this form we can relate our very simple discrimination problem to that of a “neuron.” Real neurons receive inputs from many other neurons and they “fire” when the input activity is high, thus exciting many other neurons. If we take our inputs as the elements of the augmented vector x, multiplied by the augmented weights in w, then we can sum those incoming weighted inputs into a factor, D, which represents the net activity coming into the neuron. If that factor is positive we can provide a high output of +1 (i.e. the “neuron fires”) or if the factor is negative we can provide a low output of -1 (i.e. the “neuron does not fire”). We can relate this process of firing or not to the existence of a flaw of class c1or c2. A neural network can be a large collection of interconnected “neurons” of this type (or other types). If we have a way to learn all the discriminants in such a network (called the network weights) then we have a powerful way to do pattern recognition on complex problems as well as perform other complex tasks.
We will talk more about neural nets later and describe the way we can learn to obtain the network weights but now let us describe a learning algorithm for our simple linearly separable classification problem.

## Slide 45
Two Category Training Procedure
Given an extended weight vector
and an extended feature vector
the following steps define a two class error correction algorithm
Definition: Let wk be the weights associated with xk , " feature training vectors" for cases where the class of each xk is known
(1) let
(actually, w1 can be arbitrary)
(2) Given wk, the following case rules apply
where
Notes: We can define a two category (two class) learning procedure for a problem where the two classes can be separated in a feature space x by a hyperplane. Such a problem is called a linearly separable classification problem. We start with a given set of weights which can all be zero, for example, and a set of examples (NDE tests) where we have a set of features extracted from a known flaw type. We can call these examples the feature training vectors and define a learning procedure, as shown above, where we change the weights depending on the feature vector values and the type of class present. The procedure shown above is relatively simple where we either leave the weights unchanged or change them by either adding or subtracting the feature vector values multiplied by positive constant we choose. It can be shown this learning procedure must eventually stop and produce a set of weights which separates the two classes.

## Slide 46
Two Category Learning Theorem
If c1 and c2 are linearly separable and the two class training procedure is used to define wk, then there exists an integer such that wt linearly separates c1 and c2 and hence wt+k = wt for all positive k.
Ref: Hunt, E.B., Artificial Intelligence, Academic Press, 1975.
Remark: l can be a constant or can take on particular forms. For example:
can be used and the algorithm still converges. This often speeds up the
convergence
Ref: Nilsson, N, Learning Machines, McGraw Hill, 1965.
Notes: Here is a statement of the so-called two category learning theorem. As you can see, it has been known for some time. It was not until the 1980s that more powerful learning methods became readily available for neural networks, which allowed their use in problems much more complex and practical than the linearly separable case discussed here.

## Slide 47
Example: Determine if an ultrasonic signal is from a crack or a volumetric flaw based on the following two features:
x1 = " has flashpoints" 1 = "yes", -1 = "no"
x2 = " has negative leading edge pulse" 1 = "yes", -1 = "no"
crack
volumetric
(low impedance)
volumetric
(high impeance)
-1 -1
1 1 -1
1.0
-1.0
1.0
-1.0
crack
volumetric
(low imped.)
volumetric
(high imped.)
Notes: Now, let’s show a simple example of our two class flaw classification problem where we use as two features the existence of flashpoints and a negative leading edge pulses (we could also use the positive leading edge pulse feature considered previously, so this change is not important). We see in the feature space these distinguishing features can indeed be separated by a line (in fact, many lines) which we could obtain by inspection. However, we want to use our two category learning theorem to choose such a line, so we can see the learning process in action.

## Slide 48
For simplicity, we will take b = 0, l = 1 so the learning procedure is
Give an training example ( x1 , x2 )
2. If ask "is it a crack" (Y or N)
If ask "is it volumetric" (Y or N)
3. If error (N) and
If error (N) and
w
Notes: To make things very simple we will choose b=0 and λ= 0, but these choices are not necessary. Shown is the learning procedure for this case.

## Slide 49
Suppose for this case we have the following training set:
x1 = -1 , x2 = 1 (vol)
x1 = 1 , x2 = 1 crack
x1 = -1 , x2 = -1 (vol)
….
Training example 1: vol
x1 =-1 , x2 = 1
D = 0 (since w1 = w2 =0 initially)
"is it a crack" N
w
Notes: Now, suppose we have a set of examples that we use to learn a set of appropriate weights. Shown are the first three cases in this training set and how the weights are changed when we present the first training example to the learning procedure. The separating line that is generated is shown. Note that we have not yet separated the two cases because the high impedance volumetric flaw must give us D<0, not D0 as seen here.
Now, suppose we have a set of examples that we use to learn a set of appropriate weights. Shown are the first three cases in this training set and how the weights are changed when we present the first training example to the learning procedure. The separating line that is generated is shown. Note that we have not yet separated the two cases because the high impedance volumetric flaw must give us D<0, not D≤0 as seen here.

## Slide 50
Training example 2: crack
x1 =1 , x2 = 1
D = (1)(1) + (-1)(1) = 0
"is it a crack" Y
w
no change
Training example 3: vol
x1 =-1 , x2 = -1
D = (1)(-1) + (-1)(-1) = 0
"is it a crack" N
w
no further changes
Notes: Now, we present the second and third training examples. In the second example there is no change to the weights but in the third case the line now completely separates the two classes. Further training examples will not make any changes to this line, so we have learned the discriminants.

## Slide 51
Note that this classifier can also handle situations other than which it is trained on. This "generalization" ability is a valuable property of neural nets.
For example, suppose we let
x1 = 1 "definitely has flash points"
0.5 "probably has flash points"
0 "don't know"
-0.5 "probably does not have flash points"
-1 "definitely does not have flash point"
similarly for x2
Now suppose we give our trained system an example it hasn't seen before such as a crack where
x1 = 0.5 " probably has flash points"
x2 = 0.5 " probably has a negative leading edge pulse"
" is it a crack"
Y (which is correct)
Notes: An important feature of our classifier is that it can handle situations other than just those it is trained on. For example, suppose we give the x-values something other than the +1 and -1 values used in training. In the example shown we see the classifier still works. This ability to generalize to cases not seen in the training samples is what makes neural networks such powerful tools.

## Slide 52
References
Sklansky, J., and G. Wassel, Pattern Classifiers and Trainable Machines, Springer Verlag, 1981
Pao, Y.H., Adaptive Pattern Recognition and Neural Networks, Addison Wesley, 1989
Gale, W.A., Ed., Artificial Intelligence and Statistics, Addison Wesley, 1986
Duda, R.O, Hart, P.E., and D.G. Stork, Pattern Classification, 2nd Ed., John Wiley, 2001
Fukunaga, K. Statistical Pattern Recognition, Academic Press,1990.
Webb, A, Statistical Pattern Recognition, 2nd Ed., John Wiley, 2002.
Nadler, M., and E.P. Smith, Pattern Recognition Engineering, John Wiley, 1993.
Notes: Here are some references on statistical pattern recognition. Later, we will give some references on neural networks.