## Slide 1
Linear Electrical and Acoustic Systems
– Some Basic Concepts
Notes: Linear systems play an important role in modeling ultrasonic NDE systems so we will discuss some of the basic concepts involved.

## Slide 2
Learning Objectives
Two port systems
transfer matrices
impedance matrices
reciprocity
1-D compressional waves in a solid
equation of motion/constitutive equation
acoustic transfer matrix of a layer
Single Input-Single Output systems
LTI systems
impulse response, transfer functions
convolution/ deconvolution
Wiener filter
Notes: We will see that both two port systems and single input-output systems are important types of systems for modeling ultrasonic systems for both the electrical and acoustic components.

## Slide 3
Two Port Systems
Vi
R
C
Consider a simple system again:
If we take off the voltage
source we are left with:
R
C
This is an example of a
two port system:
V1
V2
I1
I2
Notes: Here we see that an RC circuit with the voltage source removed can be modeled as a two port electrical system where we can have a voltage and current acting at both the left and right ends (ports) of the system.

## Slide 4
V1
V2
I1
I2
Transfer matrix:
V1
V2
I1
I'2 = - I2
Alternately, we can express this two port system
in terms of an impedance matrix:
Notes: For a linear two port system the voltage and current flowing into the input port can be related to the voltage and current flowing out of the output port through a 2x2 transfer matrix. Similarly, we can model the two port system in terms of a 2X2 impedance matrix where the voltages are related to the currents. However, in this case by convention we take the currents as both flowing into the system, as shown.

## Slide 5
V1
V2
I1
I2
V1
V2
I1
I2
(1)
(1)
(1)
(1)
(2)
(2)
(2)
(2)
State (1):
State (2):
Reciprocity
A
B
C
D
Notes: Consider a two port system that is connected to two sets of other systems, producing what are called states (1) and (2), as shown above. If the two port system is a reciprocal system then these voltages and currents in these two states are related through a reciprocity equation.

## Slide 6
For reciprocal systems, the impedance matrix
is symmetric, i.e.
V1
V2
I'2
I1
and the determinant of the transfer matrix is equal to one
V1
V2
I1
I2
Notes: It can be shown that reciprocity implies that the impedance matrix of the two port system is symmetric and that the determinant of the 2x2 transfer matrix is unity.

## Slide 7
Relationship between transfer matrix components and
impedance matrix components (reciprocal system)
Note:
Notes: Since the impedance matrix and the transfer matrix both describe the same two port system, they must be related. For a reciprocal system, here is how the transfer matrix components are related to the impedance matrix components.

## Slide 8
1-D plane compressional wave in an elastic solid
sx
dx
dz
dy
Constitutive equation
compressional (P)
wave speed
…stress
… displacement
Notes: Previously, we examined 1-D plane waves traveling in a fluid. Now, consider a 1-D plane compressional wave traveling in a solid where we assume the wave is traveling in the x-direction and the only stress acting in that direction is a normal stress in the x-direction We can again apply Newton’s law to relate the stress to the x-displacement. For the solid we have a stress-strain constitutive equation as shown, which can be written in terms of Youngs modulus, E, and Poisson’s ratio, ν, or equivalently, in terms of the density ,ρ, and the wave speed, cp , for compressional waves

## Slide 9
waves in a
solid layer
x = 0
x= l
l
A
B
velocity
displacement
stress
compressive force
acoustic impedance of the layer
(minus sign because
a positive stress is tensile)
Notes: The wave speed cp is indeed the wave speed of this wave in the solid since when we place the constitutive equation into Newton’s law we get the wave equation for the displacement where cp appears as the wave speed present.
Now, consider a combination of harmonic waves traveling in both the plus and minus x-directions. Shown are the expressions for the displacement, velocity and stress due to these waves. Such a combination of waves might exist, for example, in a solid layer of width l where we have waves traveling in both directions due to reflections from the ends of the layer. If we write the wave amplitudes A and B in terms of the compressive forces and velocities acting at the ends of the layer then we can relate these compressive forces and velocities at each end (port) to each other, producing the transfer matrix shown for this acoustic two port system, whose elements are functions of wave number, the length, and the acoustic impedance of the layer. The forces involved here are those forces generated over an areas S on the faces of the layer.
Thus, transfer matrices and two port systems can represent both electrical elements and acoustic wave elements of an NDE system.

## Slide 10
Equivalent transfer matrices
I1
V1
I2
V2
[T1]
[T2]
[TN]
I1
V1
[Tg]
I2
V2
Notes: If we connect a number of two port systems, then we can replace the entire collection of the system by a single 2x2 transfer matrix that is simply the matrix product of the individual transfer matrices. If the individual systems are reciprocal then the transfer matrix of the collection will also be reciprocal.

## Slide 11
When we specify termination conditions at both
ports of a two port system, we end up with a system
where single inputs and outputs are related:
Vi
R
C
I = 0 (open circiut
termination)
V0
Vi
V0
(terminated with
voltage source)
Notes: If we connect the ends of a two port system to either known sources or terminating impedances then the two port system reduces to a single input, single output system as shown for example for this RC circuit where a voltage source is placed at one end and the other end is left as an open circuit. In that case we see thesingle input, single output system relates the open circuit output voltage to the input voltage source.

## Slide 12
Vi
R
C
V0
so
Note: V0(t) is defined here in terms of Vi(t) only
implicitly as the solution of this differential equation, i.e.
L … linear operator
Notes: If we examine this RC circuit in the time domain we see we can write down a differential equation that gives the open circuit voltage in terms of the voltage source. This is a linear differential equation whose solution can be written symbolically as a linear operator acting on the voltage source to generate the open circuit voltage output.

## Slide 13
An important class of these single input-output systems
is a linear time-shift invariant (LTI) system
L
i(t)
o(t)
if
then
if
then
linearity
time-shift invariance
Notes: Since the linear operator transforms the input to the output it can be represented as a single input, single output system as shown. Since the operator here is a linear operator, we say this is a linear system where the inputs and outputs satisfy the linearity conditions shown above. If a time shift at the input produces an identical time shift at the output, then we say this is a linear time-shift invariant (LTI) system. Obviously, our RC circuit example is an LTI system. We will assume the components of an ultrasonic NDE system can be represented by LTI systems.

## Slide 14
Impulse response of LTI systems and the convolution
integral
L
d(t)
g(t)
delta
function
impulse response
function
L
i(t)
o(t)
convolution of g and i
Notes: An important characteristic of LTI systems is that if we consider a time domain delta function as the input and let g(t) be the output of the system, called the impulse response function, then the response of the LTI system to any input, i(t), can be written as the convolution integral of that input with the impulse response function. Thus, the impulse response function completely characterizes the LTI system.

## Slide 15
i(t)
t
i(t)
t
linearity and time
shift invariance
linearity
(additivity)
response to the
thin rectangle
total output
Notes: This convolution integral result follows directly by considering an arbitrary input as the sum of different strength delta functions (actually small width rectangles that approximate delta functions) and using the linearity and time shift invariance properties of the LTI system to write the output as a finite sum, which in the limit simply becomes the convolution integral.

## Slide 16
If
and
then
Notes: If we calculate the Fourier transforms of the input function and the impulse response function then one can show that the convolution integral relationship between the time domain inputs and outputs of an LTI system reduces to a multiplication in the frequency domain.

## Slide 17
convolution in the frequency domain is just
(complex-valued) multiplication
Notes: We can write the convolution integral of the input and the impulse response function in the two different equivalent forms shown . However, the input-output relationship is much more conveniently calculated in the frequency domain where we need only to perform a complex-valued multiplication. After the multiplication we can also recover the time domain output signal through an inverse FFT.

## Slide 18
G1(w)
G2(w)
GN(w)
I(w)
O(w)
The frequency components of the impulse response function
of an LTI system are also called the transfer function, t(w), for the
system since this function "transfers" the inputs to the outputs:
I(w)
O(w)
t(w)
Notes: Working in the frequency domain allows us to deal with a cascade of LTI systems that we can replace by a single transfer function, which is just the Fourier transform of the impulse response function for the entire system. Formally, the transfer function is just the ratio of the output to the input in the frequency domain.

## Slide 19
flaw
Transducer
(transmitter)
cabling
cabling
Transducer
(receiving)
Pulser
Receiver
flaw signal
Vi(w)
Ft(w)
input voltage
output force
FB(w)
force on receiver
VR(w)
output voltage
Notes: As an example of such a cascade of LTI systems, consider all the components of an ultrasonic NDE immersion system. We can consider the output to be the frequency components of the received flaw signal and the input to be the Thevenin equivalent voltage source of the pulser. Then we can write the output in terms of the input multiplied by three transfer functions that represent the sound generation process (pulser, cable, sending transducer), the wave propagation and scattering processes between the transducers, and the sound reception process (receiving transducer, cabling, and receiver). We will see later we can model all these transfer functions so we have a complete model of the entire ultrasonic NDE measurement system.

## Slide 20
deconvolution in the frequency domain is just
(complex-valued) division … but it must be
done with care
Deconvolution
Generally, a Wiener filter is used in ultrasonics applications
to desensitize the division process to noise
small "noise" constant
( )*= complex
conjugate
Notes: In principle we can obtain the transfer function by dividing the frequency components of a measured output by the frequency components of a measured input. However, while convolution, which involves multiplication in the frequency domain, is well behaved, division in the frequency domain (also called deconvolution) can be contaminated by noise, rendering the results invalid. To avoid this we use a filter to handle this problem. In ultrasonic NDE we generally use a Wiener filter which has a small noise constant, e, that we must choose.

## Slide 21
It is easier to see the Wiener filter if we rewrite the deconvolution in the form
where
Wiener filter
(1)
Notes: We can see the effects of the Wiener filter more clearly by writing the deconvolution as a product of the ordinary division by a function W that represents the filter. We will show the behavior of W on the next slide. However, note that we must not implement the deconvolution in the form of Eq. (1) above but must use the original form shown on the previous page.

## Slide 22
MATLAB example showing effects of choice of e
>> f = linspace(0, 10, 200);
>> I= f.*(f<5) +(10-f).*(f>5);
>> plot(f, I)
>> e =.01;
>> W = I.^2./(I.^2 + e^2*max(I.^2));
>> plot(f, W)
>> hold on
>> e= .1;
>> W = I.^2./(I.^2 + e^2*max(I.^2));
>> plot(f, W,'--')
>> xlabel(' frequency, f')
>> ylabel(' W')
>> hold off
e =.01
e =. 1
I
W
f
Notes: Here is an example where we model the input function as a simple triangular function. We see that the Wiener filter W for small values of the constant e is near unity so the Wiener filter does not modify the ordinary division process except at the ends where the input function becomes small. At places where the input is small, noise can contaminate the deconvolution result so the Wiener filter prevents those places from dominating the result.

## Slide 23
Homework problems
C.2, C.3
Notes: Homework problems from Appendix C.