## Slide 1
Wave Propagation Fundamentals -1
Propagation of Plane and Spherical Waves
Notes: Propagating waves are a key part of an ultrasonic NDE measurement system. Plane waves and spherical waves serve as fundamental building blocks for describing the waves seen in NDE tests so we will examine those waves here.

## Slide 2
Learning Objectives
Plane waves in fluids and solids
Elastic wave potentials
Spherical waves in fluids and solids
Notes: We will examine both plane waves and spherical waves in both fluid and elastic media.

## Slide 3
is an arbitrary plane wave"pulse" solution
of the wave equation traveling in the + x direction.
The function is a harmonic
plane wave traveling in the + x direction.
They are simply related through the Fourier Transform:
Plane Waves - Fluid
amplitude
phase
Waves in a fluid satisfy the wave equation
Notes: We have seen before that the pressure waves in a fluid satisfy the wave equation. We also saw that we could write down the general solutions of plane waves in the fluid either as pulses in the time domain or as harmonic waves in the frequency domain and we can relate those two domains through the Fourier transform.

## Slide 4
we saw previously we can write a plane harmonic wave in different forms:
For the last form we can also write
Plane Waves-Fluid
Notes: We also saw previously that we could write propagating plane harmonic waves in terms of different parameters. For solving wave problem we will generally use the forms shown above where we either use the frequency in cycles/sec or in rad/sec.

## Slide 5
Summary: for a harmonic wave of
time
dependency, a plane wave traveling in the direction
is given by (dropping the common time term)
For a plane wave traveling in an arbitrary direction , n
n
where k = k n
n x = constant
plane
.
Plane Waves-Fluid
is called the
wavenumber vector
Notes: Since all the harmonic waves have the same time dependency, which here is exp(-iωt), generally we will drop that common term and assume it is always implicitly present. All our plane wave results shown are for waves traveling in the plus or minus x-direction but we can easily write similar plane wave solutions for a wave traveling in an arbitrary direction, n, in three dimensions.

## Slide 6
Plane Waves - Fluid and Solid Media
n
Waves in a fluid are governed by the scalar wave equation
Waves in an isotropic elastic solid are governed by the
vector Navier's equations
u … displacement vector
l, m … Lame constants
r … density
(direction of propagation)
Notes: Here we show a general plane wave traveling in a fluid, where it is satisfies the scalar wave equation for the pressure. In an elastic solid, general waves are governed by Navier’s equations for the displacements, not a wave equation directly. Navier’s equations depend on the density, ρ , of the solid and two elastic Lame constants, λ, and μ.

## Slide 7
n
u
n
d
u
Navier's equations also have plane wave solutions. There are
two types – P-waves and S-waves. These are "bulk" waves.
compressional
(P) waves
shear
(S) waves
polarization
Plane Waves-Solid
Notes: Like a fluid, Navier’s equations do have plane wave solutions. However, in a solid there are actually two types of solutions called P-waves and S-waves, which differ in their direction of displacement (called the polarization) and in their wave speed. The wave speed cp is the P-wave speed and the wave speed cs is the S- (shear) wave speed. Since both types of these waves travel in the bulk of a material, they are also called bulk waves. For most solids the P-wave speed is about twice the S- wave speed.

## Slide 8
Plane Waves-Solid
Polarizations
Plane P-waves are longitudinally polarized
in the direction of propagation
Plane S-waves are polarized in the plane
perpendicular to the direction of propagation.
SV
SH
Vertically polarized S-waves are called
SV-waves while horizontally polarized
S-waves are called SH waves
Notes: Plane P-waves are polarized in the direction of propagation while plane S-waves have a polarization in a plane perpendicular to the direction of propagation. If we take that polarization plane as a vertical plane then we can consider either vertically polarized S-waves, called SV-waves, or horizontally polarized S-waves called SH-waves.

## Slide 9
Plane Waves-Solid
Bulk wave speeds
E … Young's modulus
n … Poisson's ratio
G = m .. Shear Modulus
Compressional wave speed in a bar
Compressional wave speed in a plate
Notes: Bulk P- and S-waves travel with different wave speeds which can be written either in terms of the Lame constants of the elastic solid or Young’s modulus, E, and Poisson’s ratio , ν. For S-waves we can also write the shear wave in terns of the shear modulus, G, which is related to E and ν.
We should note that if we generate waves traveling in thin geometries like bars or plates, the P-waves travel with wave speeds different from the bulk wave speeds while the S-wave wave speed is unaffected. Shown are the P wave speeds for a bar and plate.

## Slide 10
Although Navier's equations are not wave equations, solutions
to Navier's equations can be found in terms of potential functions
that do satisfy wave equations
f … scalar potential
y … vector potential
P-waves
S-waves
Plane Waves-Solid
Notes: In Navier’s equations we do not see directly wave equations. However, if we use the Helmholtz decomposition and represent the displacement in terms of potentials, then we do see separate wave equations for the P-waves and S-waves. Thus, solutions of elastic wave problems are often obtained in terms of these potentials.
Note that P-waves are also called compressional waves, longitudinal (L-waves), pressure waves, primary waves, dilatational waves, or irrotational waves while S-waves are also called shear waves, tangential or transverse (T-waves), secondary waves, equivoluminal waves, or rotational waves.

## Slide 11
Material | Compressional (P-wave) wave speed (m/s x 103) | Shear (S-wave) wave speed (m/s x 103) | Density r (kgm/m3 x 103) | Impedance (P-wave) ( kgm/(m2-s) x 106)
Air | 0.33 | -- | 0.0012 | 0.0004
Aluminum | 6.42 | 3.04 | 2.70 | 17.33
Brass | 4.70 | 2.10 | 8.64 | 40.6
Copper | 5.01 | 2.27 | 8.93 | 44.6
Glass | 5.64 | 3.28 | 2.24 | 13.1
Lucite | 2.70 | 1.10 | 1.15 | 3.1
Nickel | 5.60 | 3.00 | 8.84 | 49.5
Steel, mild | 5.90 | 3.20 | 7.90 | 46.0
Titanium | 6.10 | 3.10 | 4.48 | 27.3
Tungsten | 5.20 | 2.90 | 19.40 | 101.0
Water | 1.48 | -- | 1.00 | 1.48
Table D.1 Acoustical properties of some common materials.
In the S.I. system 1 Rayl = 1kg/m2-s so these values are in units of 106 Rayl or MRayl
Notes: Here is a short table illustrating the compressional and shear wave speeds, densities, and the specific acoustic impedances for P-waves of some common materials. Generally we see that compressional waves travel about twice as fast as shear waves. Also note that specific acoustic impedances are often given in units of megaRayls (MRayl) which units are defined above.

## Slide 12
Elastic Wave Potentials
For two-dimensional waves
displacements
stresses
Plane Waves-Solid
Notes: Potentials are often used to solve wave equations in elastic solids analytically. For 2-D problems one only needs to use scalar P-wave and S-wave potentials and those potentials (which are not physical quantities) can be related to the displacements and stresses as shown.

## Slide 13
Plane Waves-Solid
Plane wave solutions
x
potential
displacement
velocity
normal stress
P-waves
Notes: In an elastic solid we can consider plane P-wave solutions for the potential or we can consider the corresponding solution in terms of the displacement, the velocity, or the normal stress. All these waves have the same form where the amplitudes are related to each other as shown. Note that the stress and velocity amplitude relationship is like that of the pressure and velocity relationship except that there is a minus sign present because normal stress is defined to be positive when it is a tensile stress.

## Slide 14
Plane Waves-Solid
x
s
S-waves
potential
displacement
velocity
shear stress
Notes: In an elastic solid we can consider plane S-wave solutions for the potential or we can consider the corresponding solution in terms of the displacement, the velocity, or the shear stress. All these waves have the same form where the amplitudes are related to each other as shown. Note that in the shear wave case the polarization vector of the potential and the polarization vector of the displacement (or velocity) are different but they both lie in the plane of the wavefront and can be related to each other.

## Slide 15
Spherical waves arise physically from "point" sources. If a
point source emits waves uniformly in all directions, then we
expect the waves to depend only on the radial distance, r , from
the point source.
r
Spherical Waves-Fluid
Notes: Plane waves are important building blocks for modeling the propagation of waves. We will see that spherical waves are likewise a key type of building block. Physically, a spherical wave in a fluid can be though of as the waves arising from a point source that emits waves uniformly in all directions so that the waves depend only on the radial distance from the source.

## Slide 16
Consider spherical harmonic waves of exp(-iwt) time
dependency. The equation of motion of the fluid and the
wave equation are given by
In terms of the distance, r, from the source, in spherical
coordinates these equations are
Spherical Waves-Fluid
Notes: For harmonic spherical waves in a fluid Newton’s law and the wave equation reduce to the forms shown.

## Slide 17
There are two solutions of the wave equation of the
form
The first term represents a wave traveling in the outward
radial direction while the second term represents a wave
converging on the source. Since the source only generates
outward going waves, we must set B = 0. The pressure and
radial velocity in the out going wave are then
Spherical Waves-Fluid
Notes: We can obtain solutions to the wave equation representing either outgoing waves from a point source or spherical waves that converge to the point. For the outgoing waves we have the forms shown for the pressure and velocity.

## Slide 18
In many cases we are only interested in the waves many
wavelengths from the source, in which case kr >> 1 and we
can write approximately
Compare this to a plane wave traveling in the +z direction where
Spherical Waves-Fluid
r
z
Notes: If we are primarily interested in the waves many wavelengths from the source, then the factor kr >>1 and the pressure and velocity take the simpler forms shown above. These look very similar to the plane wave case except for the 1/r spreading factor which is absent in the plane wave case and causes the amplitude of the spherical wave to become smaller as the distance from the source increases.

## Slide 19
Spherical Waves-Elastic Solid
Spherical waves from point sources in an elastic solid have a
more complex structure in general, but for kr >>1 they are
similar to that of a fluid:
A
B
r
P-wave
S-wave
Notes: In elastic solids, P- and S- waves from a point source have a more complex behavior but for kr >>1 the displacement in the waves has a radial dependency that looks much like that in a fluid. The amplitudes are now vector quantities that are functions of the angles present in a spherical coordinate system and have polarization vectors that are either in the radial direction, A, of propagation (for P-waves) or in a direction, B, orthogonal to that radial direction (for S-waves).