## Slide 1
Special Topics – 1
Dispersion
Notes: Here we will briefly describe wave dispersion

## Slide 2
Learning Objectives
Definition of dispersion
Group velocity
Examples
Notes: We will define dispersion and the group velocity of waves. We will also give an example of the effects of dispersion on waves as they propagate.

## Slide 3
Dispersive Waves and the Group velocity
Recall that the wave number k, and the frequency, w, were related to
the (phase) velocity, c, through the relationship
If the phase velocity, c, is a function of frequency then we say that the wave is dispersive and the wave number is
and we have
where cg is called the group velocity.
The group velocity can be shown to be the speed at which the energy in a dispersive wave propagates.
w … frequency in rad/sec
Notes: For propagation problems where the wave speed is a constant, the wave number varies linearly with the frequency. However, if the wave speed itself is a function of frequency, then the wave number is a more complex function of frequency and its derivative with respect to frequency is the reciprocal of the group velocity. Physically, the group velocity is the wave speed at which energy propagates in a wave. The frequency dependent wave speed itself is called the phase velocity.

## Slide 4
where f is the frequency in cycles/sec (Hz)
If A(f) is the Fourier transform of a(t) then we have for a propagating non-dispersive plane wave traveling in the +x direction with a constant phase velocity, c,
However, if the phase velocity is a function of frequency then as the wave propagates with its energy traveling with the group velocity and its profile changes with increasing distance
Group velocity
Notes: Here is the group velocity expressed in terms of the phase velocity and its derivative.
The superposition of non-dispersive harmonic waves through the use of the inverse Fourier transform produces a traveling wave in the time domain that always has the same profile. The superposition of dispersive harmonic waves, however, generates a traveling waveform whose shape changes.

## Slide 5
0
1
2
3
4
5
6
7
8
9
10
-2
0
2
4
6
8
10
12
Propagation distance x = 0
t, msec
mm/msec
f in MHz
Notes: To see an example of dispersion, consider a waveform which starts out at x = 0 with a “box” profile in time, as shown. Let the wave speed (of the medium it is propagating in) have the simple linear dependency on frequency, as shown.

## Slide 6
0
1
2
3
4
5
6
7
8
9
10
-6
-4
-2
0
2
4
6
8
10
12
14
Propagation distance x = 10 mm
t, msec
Notes: If one computes the inverse Fourier transform when the wave is at x = 10 mm, the waveform has changed dramatically, with significant ringing preceding and within the wave form itself. The dotted red line would be the waveform if it traveled in a non-dispersive medium at 6 mm/ microsec.

## Slide 7
0
1
2
3
4
5
6
7
8
9
10
-6
-4
-2
0
2
4
6
8
10
12
14
Propagation distance x = 30 mm
t, msec
Notes: At x = 30 mm the wave distortions are even more pronounced.

## Slide 8
0
1
2
3
4
5
6
7
8
9
10
-6
-4
-2
0
2
4
6
8
10
12
14
Propagation distance x = 50 mm
t, msec
Notes: At x = 50 mm again there are continuing wave form changes. The large ringing see at earlier times comes from the fact that the higher frequencies travel with higher wave speeds in this case so they run ahead of the main wave form.
Waves traveling in plates, pipes, and shells (called guided waves) inherently are dispersive so that guided wave NDE inspections must deal with the effects of dispersion.