## Slide 1
Wave Propagation Fundamentals -2
Reflection and Transmission
Notes: NDE immersion tests involve multiple media ( i.e. a fluid and solid) so it is important to understand how waves reflect and transmit at the interfaces between different media.

## Slide 2
Learning Objectives
Reflection and transmission coefficients
Snell's law
critical angles
acoustic impedance
amplitudes/intensities
inhomogeneous waves
Stokes' relations
Fluid-fluid and fluid-solid examples
Notes: In this section we will see how plane waves reflect and transmit at planar interfaces between fluids or between fluids and elastic solids. It will be shown that there are a number of important concepts that govern reflection/transmission behavior including Snell’s law, critical angles, and Stokes relations. In some cases we will give detailed derivation of results but in other cases we will simply state important results without proof.

## Slide 3
x
y
Fluid-Fluid Problem
incident wave
reflected wave
transmitted wave
pressure in the:
Notes: Consider the problem of the reflection of a plane pressure wave (traveling at an angle as shown) from a plane interface between two different fluids. This case is normally not encountered in practice but it will be a simple case that captures much of the physics involved in more practical cases. An incident harmonic wave will generate reflected and transmitted plane waves whose solutions we can write as indicated above., where we will drop the common exp(-iωt) terms.

## Slide 4
x
y
from the equation of motion , so
Notes: In the first medium the incident and reflected waves are present while in the second medium we only have a transmitted waves. From Newton’s law we can relate the derivative of the pressure in the y-direction to the velocity component in that direction, so taking the derivatives of the pressure expressions in the two media we can obtain the y-velocity expressions for those media.

## Slide 5
Boundary conditions: on y = 0
Phase matching:
angle of incidence
= angle of reflection
Snell's law
Notes: At the interface ( y = 0) the pressure and the y-component of the velocity must be continuous (but the x-component of the velocity need not be continuous because we are modeling the fluids as ideal (i.e. non-viscous) fluids). Placing our pressure and velocity expressions into these boundary conditions we obtain the two equations shown. Since we must have these equations satisfied for all x we must have their phase terms all match which leads to two results: the angle of incidence must be equal to the angle of reflection, and the incident and transmitted wave angles must satisfy Snell’s law.

## Slide 6
Solving, we find the transmission and reflection
coefficients (pressure ratios)
or, in terms of velocity ratios
Notes: Eliminating the common phase terms gives us two equations for the reflected and transmitted wave amplitudes which we can solve to determine the transmission and reflection transmission components (based on pressure amplitude ratios). Using the plane wave relationship between pressure and velocity amplitudes we can alternately express those transmission and reflection coefficients in terms of velocity ratios.

## Slide 7
Special Case - normal incidence
za = rc … plane wave specific impedance
void
rigid
Rv = -1
Rv = 1
Notes: In the special case where the incident plane wave strikes the plane interface at normal incidence the velocity based transmission and reflection coefficients are of a much simpler form. We see that these coefficients are controlled by the plane wave specific acoustic impedances.
If the second medium is a void (a free surface), then the reflection coefficient is just -1, showing the incident wave is totally reflected with a change in sign. However, the velocity polarization of the reflected wave was taken in this case to be in the –y direction so that the y-velocity at the free surface is actually double that of the incident wave. In contrast, the total pressure due to the incident and reflected wave amplitudes is zero, as it should be since we have a free surface.
If the second medium is taken to be an infinitely rigid medium, then the reflection coefficient is +1 and so the total y-velocity at the rigid interface is just zero. The pressures of the incident and reflected waves, however, add so that the total pressure at the interface is just double that of the incident wave.

## Slide 8
Let c2 > c1 . Then for
Critical angle
Whereas for
transmitted plane wave
inhomogeneous wave
y
x
y
x
Notes: If the wave speed of the second medium is higher than the wave speed in the first medium (containing the incident wave) then we will see that there is critical angle, sin-1(c1/c2) , which controls the behavior of the transmitted wave. For incident angles less than the critical angle the expression for the cosine of the transmitted angle (which involves a square root) is real so that we just see an ordinary plane wave expression for the transmitted wave. However, if the incident angle exceeds the critical angle then the cosine of the transmitted wave becomes imaginary. Depending on whether the frequency is positive or negative, we must change the sign on this cosine term so that the pressure never grows exponentially large in the y-coordinate, which would give an unphysical behavior. Thus, in this case we get a wave traveling parallel to the interface with an exponentially decreasing amplitude away from the boundary. This is called an inhomogeneous wave.
For there to be a critical angle the second medium must be the faster medium since there is no critical angle where sin-1(c1/c2) is real if the second medium is slower than the first.

## Slide 9
Relationship between amplitudes and intensities
Intensity, I , = time average power flux in the wave
P … pressure amplitude
V … velocity amplitude
Solid:
Fluid:
P-wave
S-wave
Tnn … normal stress amplitude
Tns … shear stress amplitude
Vn .. normal velocity amplitude
Vs … tangential velocity amplitude
Notes: In some cases we want to know the energy being carried in a harmonic wave. We can represent such energy through an intensity, I, which defines a time average power flux in the wave. Shown are expressions for the intensities of a plane wave travelling in a fluid or a solid in terms of the underlying amplitudes of pressure, velocity, or stress.

## Slide 10
Stokes' Relations
T12
T21
reversed path
Fluid-fluid
Notes: In a pulse-echo inspection the same transducer is used as both a transmitter and receiver of ultrasound. In that case the waves that are scattered from a flaw back to the transducer follow a completely reversed path from the incident waves. and there can be transmission coefficients involved in both directions. One can show that in the case of two fluids these transmission coefficients are related through the Stokes relations given above.

## Slide 11
Stokes' Relations
reversed paths
Fluid-solid
P
S
P
P
P
S
Notes: If we consider a fluid-solid interface, since there can be both P-waves and S-waves in the solid we have the two Stokes relations given above. Note that we are taking the incident wave to be propagating in a vertical plane here. In this case we can show that the S-wave will have its polarization also in that plane and we will call it an SV-wave.

## Slide 12
Transmission Coefficients (Fluid-Solid interface)
based on velocity ratios
P
S
P
fluid
solid
Notes: We can solve for the plane wave reflection and transmission coefficients at a fluid-solid interface in the same manner as done for the fluid-fluid interface but with more algebra. In an immersion inspection the waves are generated in a fluid, so we are primarily interested in the transmission coefficients into the solid component being inspected. Shown are those transmission coefficients based on velocity ratios.

## Slide 13
Fluid-Fluid R, T coefficients
(magnitude) water-steel
pressure-based
R
T
>> ang = linspace(0, 89.9, 200);
>> [R,T] = pressure_coeffs(1.0, 7.9, 1480, 5900, ang);
>> plotyy(ang, abs(R), ang, abs(T), @myplot1, @myplot2)
>> xlabel('angle, degrees')
>> ylabel('|R|')
0
10
20
30
40
50
60
70
80
90
0.9
1
1.1
angle, degrees
|R|
0
10
20
30
40
50
60
70
80
90
0
1
2
|T|
critical angle
Notes: Here are some MATLAB results showing the refection and transmission coefficients obtained for a fluid-fluid interface where the first medium was water and the second fluid P-wave speed was taken to be the same as the compressional wave speed of steel. One can see a critical angle here at about 15 degrees.

## Slide 14
Fluid-Fluid R, T coefficients
(phase) water-steel
pressure-based
>> plot(ang, unwrap(angle(R)), ang, unwrap(angle(T)), '--')
>> xlabel('angle, degrees')
>> ylabel('phase of R, T')
R
T
0
10
20
30
40
50
60
70
80
90
-3.5
-3
-2.5
-2
-1.5
-1
-0.5
0
angle, degrees
phase of R, T
Notes: Here is the same fluid-fluid model results for the phase of the reflection and transmission coefficients. Note that below the critical angle the coefficients are real so the phase angles are zero.

## Slide 15
0
10
20
30
40
50
60
70
80
90
0.93
0.94
0.95
0.96
0.97
0.98
0.99
1
1.01
0
10
20
30
40
50
60
70
80
90
0
0.01
0.02
0.03
0.04
0.05
0.06
0.07
0.08
angle, degrees
|R|
Fluid-Fluid R, T coefficients
(magnitude) water-steel
velocity-based
>> [R,T] = velocity_coeffs(1.0, 7.9, 1480, 5900, ang);
>> plotyy(ang, abs(R), ang, abs(T), @myplot1, @myplot2)
>> xlabel('angle, degrees')
|T|
R is same as
for pressure,
T is much
smaller
|R|
|T|
Notes: If we use reflection and transmission coefficients based on velocity ratios, then the reflection coefficient stays the same but the transmission coefficient is much smaller.

## Slide 16
Fluid-Fluid R, T coefficients
(phase) water-steel
velocity-based
>> [R,T] = velocity_coeffs(1, 7.9, 1480, 5900, ang);
>> plot(ang, unwrap(angle(R)), ang, unwrap(angle(T)), '--')
>> xlabel('angle, degrees')
R
T
phases are same
as for pressure
0
10
20
30
40
50
60
70
80
90
-3.5
-3
-2.5
-2
-1.5
-1
-0.5
0
angle, degrees
Notes: The phases for the velocity ratios are the same as for the pressure ratios.

## Slide 17
vinc
vreflt
vtrans
Fluid-Solid Tpp coefficient
(magnitude) water-steel
velocity-based with cs =0
>> [tpp,tss] = trans2(ang,1.0, 7.9,1480,5900,0);
>> plot(ang, abs(tpp))
>> xlabel('angle, degrees')
>> ylabel(' |tpp|')
same as for
fluid-fluid
model
0
10
20
30
40
50
60
70
80
90
0
0.01
0.02
0.03
0.04
0.05
0.06
0.07
angle, degrees
|tpp|
Notes: Here is the transmission coefficient for P-waves using the full solid model for a water-steel interface but where we set the shear wave speed of the solid to be zero. In this case, we do recover the fluid-fluid result

## Slide 18
Fluid-Solid Tpp coefficient
(phase) water-steel
velocity-based with cs =0
>> plot(ang, unwrap(angle(tpp)))
>> xlabel('angle, degrees')
>> ylabel('phase of tpp, radians')
same as for
fluid-fluid
model
0
10
20
30
40
50
60
70
80
90
-1.6
-1.4
-1.2
-1
-0.8
-0.6
-0.4
-0.2
0
angle, degrees
phase of tpp, radians
Notes: The phase is also the same for the fluid-solid and fluid-fluid models in this water-steel case.

## Slide 19
Fluid-Solid tpp ,tps
coeffs (mag) water-steel
velocity-based
0
10
20
30
40
50
60
70
80
90
0
0.5
1
1.5
2
2.5
3
3.5
angle, degrees
First critical
angle
Second critical
angle
| tpp |
| tps |
>> [tpp, tps] = trans2(ang, 1.0, 7.9, 1480, 5900, 3200);
>> plot(ang, abs(tpp), ang, abs(tps), '--')
>> xlabel('angle, degrees')
Notes: Here now are the actual fluid-solid results for both transmitted P-waves and S-waves, showing the magnitude of the transmission coefficients based on velocity ratios. We see that there are two angles where the behavior changes. These are critical angles which we will describe shortly.

## Slide 20
Fluid-Solid tpp ,tps
coeffs (mag) water-steel
velocity-based (below
second critical angle)
0
5
10
15
20
25
30
0
0.02
0.04
0.06
0.08
0.1
0.12
0.14
0.16
0.18
angle, degrees
>> ang =linspace(0, 27, 200);
>> [tpp, tps] = trans2(ang, 1.0, 7.9, 1480, 5900, 3200);
>> plot(ang, abs(tpp), ang, abs(tps),'--')
>> xlabel('angle, degrees')
| tpp |
| tps |
Notes: This is an expanded view of the transmission coefficients below the second critical angle. We see that the P-P coefficient is nearly a constant up to near the first critical angle while P-S coefficient has a linearly increasing behavior.

## Slide 21
0
5
10
15
20
25
30
-2
-1
0
1
2
3
4
5
angle, degrees
Fluid-Solid tpp ,tps
coeffs (phase) water-steel
velocity-based
>> plot(ang, unwrap(angle(tpp)), ang, unwrap(angle(tps)),'--')
>> xlabel('angle, degrees')
tpp
tps
phase on tps
initially is p
since velocity comp.
of transmitted
S normal to the
interface is
so polarization is
assumed polarizations:
Notes: Here are the phases of the transmitted waves. Below the first critical angle the phase of the P-to-P coefficient is zero but the P-S coefficient has a phase of pi. This occurs because the actual polarization of the transmitted wave is opposite to that of the assumed polarization and recall exp(i π) =-1 so this phase of π just means the amplitude of motion in the wave is in a direction opposite to that we assumed.

## Slide 22
function [R,T] =pressure_coeffs(d1, d2, c1, c2, ang)
iang = (ang.*pi)./180;
sint =(c2/c1)*sin(iang);
cost = sqrt(1-sint.^2).*(sint <= 1) + i.*sqrt(sint.^2 -1).*(sint > 1);
R = ((c2*d2).*cos(iang) - (c1*d1).*cost)./ ...
((c2*d2).*cos(iang) + (c1*d1).*cost);
T = ((2*d2*c2).*cos(iang))./((c2*d2).*cos(iang) + (c1*d1).*cost);
Fluid-fluid R,T coefficients, pressure-based
Fluid-fluid R, T coefficients, velocity-based
function [R,T] =velocity_coeffs(d1, d2, c1, c2, ang)
iang = (ang.*pi)./180;
sint =(c2/c1)*sin(iang);
cost = sqrt(1-sint.^2).*(sint <= 1) + i.*sqrt(sint.^2 -1).*(sint > 1);
R = ((c2*d2).*cos(iang) - (c1*d1).*cost)./ ...
((c2*d2).*cos(iang) + (c1*d1).*cost);
T = ((2*d1*c1).*cos(iang))./((c2*d2).*cos(iang) + (c1*d1).*cost);
Notes: Here are the MATLAB functions for the fluid-fluid models we have discussed.

## Slide 23
function [tpp,tps] = trans2(inc, d1, d2, cp1, cp2, cs2)
iang = (inc.*pi)./180;
sinp = (cp2/cp1)*sin(iang);
sins =(cs2/cp1)*sin(iang);
cosp= (i*sqrt(sinp.^2 - 1)).*(sinp >= 1) + (sqrt(1 - sinp.^2)).*(sinp < 1);
coss = (i*sqrt(sins.^2 - 1)).*(sins >= 1) + (sqrt(1 - sins.^2)).*(sins < 1);
denom = cosp + (d2/d1)*(cp2/cp1)*sqrt(1-sin(iang).^2).*(4.*((cs2/cp2)^2).*(sins.*coss.*sinp.*cosp) ...
+ 1 - 4.*(sins.^2).*(coss.^2));
tpp = (2*sqrt(1 - sin(iang).^2).*(1 - 2*(sins.^2)))./denom;
tps = -(4*cosp.*sins.*sqrt(1 - sin(iang).^2))./denom;
Fluid-Solid P-P, P-S transmission coefficients
Notes: Here is the MATLAB function for the fluid-solid model transmission coefficients.